[This is a summary of the slides presented by Roger Shepherd of
INMOS Ltd, Bristol, UK at the T9000 systems workshop given at the
University of Kent on the 14th and 15th of September 1992 presented
by the World occam and Transputer User Group (WoTUG) in association
with COMETT and the Software Environments for Parallel Computing
(SEPC) Initiative.

We have edited the slides slightly to make them more understandable
without the pictures and corrected a few typographical errors.

The information below is (C) Copyright 1992 INMOS Ltd, UK and is
presented with permission of INMOS.

The University of Kent at Canterbury and INMOS make no claims for the
validity of the information presented below and accepts no liability
for mistakes.

Transcribed by David Beckett (djb1@ukc.ac.uk) on 21st October 1992
]

[1]
				T9000
			 An Introduction
		Roger Shepherd - INMOS Ltd. Bristol


[2]

T9000 - Designed for concurrency.

Topics:	Virtual Channels
	Memory Systems
	Processor Pipeline
	Process Model
	Configuration
	Control Links


[3]

T9000 - Virtual Channels

The links of the T2/T4/T8 generation products provide 2 channels per
link, one in each direction. Thus:

	1. A single T805 can be directly connected to at most 4
	   others.
	2. At most 8 processes on a T805 may use a channel
	   implemented by a link.

Even when the PHYSICAL (processor to processor) connectivity is
sufficient, the LOGICAL (process to process) connectivity may not be.


[4]

Example of an array:
{Figure of a square grid of processes, each process computing a
single element of the array of results}

{P.Thompson adds: The point here is that if we want to allocate, say,
four processes to each processor then each processor needs 8 links!}

[5]

T9000 - Virtual Channels - packetisation

The T9000 implements 64K virtual links; each virtual link provides a
virtual channel in each direction between two T9000 transputers.

	-----------------------
	| HEADER | DATA | EOX |
	-----------------------

Packets for different channels may be interleaved over a physical
link, allowing concurrent operation of many virtual channels.

To the programmer, a virtual channel appears just like any other
channel.


[6]

T9000 - Virtual Channels - VCP

The Virtual Channels are implemented by a second processor, the
Virtual Channel Processor (VCP).

The VCP performs packetisation etc whilst the CPU continues with
other processing.

The T9000 has a separate scheduler which schedules processes which
have completed external communications on behalf of the VCP.  The
scheduler operates concurrently with the VCP and the CPU.


[7]

T9000 - Virtual Channels - Routing

In addition to being directly connected, T9000 links may be connected
via a C104 packet router.

{Figure of many T9000s connected to a single C104}

The C104 uses packet headers to route packets to their destination.

Using a network of C104s, channels may be established between
unlimited numbers of T9000s.


[8]

T9000 - Virtual Channels - Performance

At 100 Mbit/s the T9000 links achieve the following data rates:

	with 1 byte headers:	    9.55 MBytes/second unidirectional
				2 x 8.74 Mbytes/second bidirectional

	with 2 byte headers:	    9.26 MBytes/second unidirectional
				2 x 8.27 Mbytes/second bidirectional


[9]

T9000 - Memory hierarchy

	-------   -------------   -----------
	| VCP |   | SCHEDULER |   |   CPU   |
	-------   -------------   -----------
	   |            |         |   |    |
	   |            |         ^   v    ^
	   |            |      ----------- |
	   |            |      |Workspace| |
	   |            |      |Cache    | |
	   |            |      ----------- |
	   |            |         |   |    |
	   |            |         ^   v    |
	   |            |         |   |    |
	-------------------------------------
	|          MAIN   CACHE             |
	-------------------------------------
	                |
	-------------------------------------
	|       EXTERNAL  MEMORY            |
	-------------------------------------


[10]

T9000 - Memory access capabilities of subsystems

CPU       - up to 4 accesses per cycle
VCP       - up to 3 accesses per cycle
Scheduler - up to 1 access per cycle


[11]

T9000 - Multibanked memory system

(Physical) address space is divided into 4 banks:

	bank 0 is selected by bits 5 and 4 being 00
	bank 1 is selected by bits 5 and 4 being 01
	bank 2 is selected by bits 5 and 4 being 10
	bank 3 is selected by bits 5 and 4 being 11

Each bank contains 4Kbytes of cache memory

All banks may operate concurrently.


[12]

T9000 - Memory architecture diagram

                  |          |          |          |
-----------|------o----------o----------o----------o-
|CPU       |------o----------o----------o----------o-
|          |------o----------o----------o----------o-
-----------|------o----------o----------o----------o-
                  |          |          |          |
-----------|      |          |          |          |
|Scheduler |------o----------o----------o----------o-
-----------|      |          |          |          |
                  |          |          |          |
-----------|------o----------o----------o----------o-
|VCP       |------o----------o----------o----------o-
-----------|------o----------o----------o----------o-
                  |          |          |          |
-----------|      |          |          |          |
|External  |------o----------o----------o----------o-
|Memory    |      |          |          |          |
-----------|      |          |          |          |
              ---------  ---------  ---------  ---------
              |Cache  |  |Cache  |  |Cache  |  |Cache  |
              |Memory |  |Memory |  |Memory |  |Memory |
              ---------  ---------  ---------  ---------  
               Bank 0     Bank 1     Bank 2     Bank 3


[13]

T9000 - Processor Pipeline

Processor operates by forming "groups" of instructions e.g.

	ldl; ldnl; ldl; ldnl; add

and executing these on a pipeline.

Fetch &  Local    Address  Main     ALU/FPU  Write
Group    Cache             Cache
-------  -------  -------  -------  ------   ------
|     |  |     |->|     |->|     |->|     |  |    |
|     |->|-----|  |-----|  |-|---|  |     |->|  | |
|     |  |     |->|     |->| |   |->|     |  |  | |
-------  -------  -------  -----|-  -------  ---|--
   |                         |  |               |
   ^  Groups                 ^  ^               V
   |                         |  |               |
  Read                    Read  Read          Write


[14]

T9000 - Processor performance

Speed achieved via grouping / pipelining and fast functional units.

eg. fpadd 2 cycles, fpmul 2 cycles, shsl/shr 1 cycles, mul 2-5

Peak 200 MIPS		- limited by instruction fetch rate
     25 MFLOPS		- limited by add/mul time

In practice, we can achieve >50% of these figures.


[15]

T9000 - Process model enhancements

0 - Virtual Channels
1 - Per-process error handling
2 - Resource channels and Semaphores
3 - P-Processes - protection and memory management
4 - Improved access to and control of transputer scheduler


[16]

T9000 Configuration

The T9000 is highly configurable - often "soft" configurable:

	External Memory Interface - bank address, width and timing

	VCP - header size, number of virtual channels and link speeds

	Cache - cache/RAM split

This is achieved via "configuration registers" which are accessed via
the control link or the processor executing ldconfig / stconfig
instructions.


[17]

T9000/C104 Control Links

Replacement for/enhancement to the T2/T4/T8 Reset/Error/Analyse.

Allows programming of C104 packet routers.

--------------
| Controller |-----\ /---------\ /---------\
--------------     | |         | |         |
                ___V_V___   ___V_V___   ___V_____
   Daisy        | | | | |   | | | | |   | | | | |
   chain        | ----- |   | ----- |   | ----- |
   diagram      | T9000 |   | T9000 |   | T9000 |
                |       |   |       |   |       |
                ---------   ---------   ---------

The controller sees a virtual link to each T9000.


[18]

T9000 Control Links

The T9000 Control link permits:

	Peek and poke to memory (as T2/T4/T8)
	Peek and poke to configuration registers
	Loading of blocks of code
	Start processor executing
	Start VCP executing
	Stop processor/VCP (analyse)
	Reset

	Reporting of errors