Protection and error handling
 
The IMS T9000 extends the error handling of earlier transputers to allow
error conditions to be easily trapped and handled in software. It can run
code in a protected mode where all memory accesses are checked and certain,
privileged, instructions cannot be executed.
 
--------------------------------------------------------------------------

Error handling
 
The first transputers have only a global mechanism for trapping errors;
stopping the entire processor when an error is detected. The IMS T9000
extends this to allow a trap handler to be associated with a process to
provide more localized error handling. When an error occurs, control is
transferred to the trap handler with information about the nature of the
error and where it occurred.
 
The action of a trap handler will, in general, be dependent on the language
or operating system being used and will be invisible to the applications
programmer. Some languages may include support for user written error
handlers. After taking the appropriate action, for example to report or
correct the error, the trap handler can return control to the process which
caused the error which can then continue execution. Each process can have
its own trap handler, or one trap handler can be shared by several (or all)
of the processes on the transputer.
 
To maintain compatibility with earlier transputers, the IMS T9000 can also
run processes in a global error mode where the behavior on error is
identical to the IMS T805. These two types of processes are known as
L-processes and G-processes (for Local and Global error handling)
respectively. Both L- and G-processes can be run in parallel, the processor
dynamically switching modes as it switches between processes. This allows
code compiled for the IMS T805 (which will always be in global error mode)
to be run in parallel with code specifically compiled for the IMS T9000.
 
-----------------------------------------------------------------

Protected mode
 
The IMS T9000 can also run code in protected mode. This is designed to
allow run-time checking of programs written in `unsafe' languages such as C
and also to provide memory management. For example, C allows pointers to
data or functions. Without checks for valid pointers, these could contain
an illegal memory address such as: another process's data or code; a non
word aligned address; or a function pointer which does not point to valid
code. As no checks are defined in the language it is important to be able
to check such accesses at run time, if needed.
 
The protection mechanism is intended to support software development  and
debugging, and programming secure systems. It protects the user's processes
or tasks from each other and also protects an operating system kernel, or
other run time support, from user code. Although code run in this mode is
frequently referred to as a `protected process', it is not the process
which is protected but the rest of the world that is protected from errors
in the process.
 
Protected mode processes
------------------------
 
Any L-process can run a piece of code as a protected mode process (or
P-process); the processor saves the state of the L-process and starts
executing the P-process. The P-process is executed until control is
returned to the L-process because of an error, protection violation or some
other reason. It is important to realize that P-processes are not scheduled
by the transputer's own scheduler - they only run under the control of a
supervisor L-process. Any of the instructions or other events that might
cause a P-process to be descheduled, will cause control to be returned to
the supervisor. The relationship between a P-process and its supervisor is
analogous to that between an L-process and its trap-handler. In both cases
the processor can be thought of as swapping between the two pieces of code.
 
Executing illegal instructions
------------------------------
 
Because control is returned to the supervisor when a P-process attempts to
execute a privileged or illegal instruction, it is possible to provide
communication and other facilities to a P-process in a controlled way, but
one which is invisible to the programmer. For example, the input and output
instructions are privileged so, if a P-process attempts a communication
then it will trap to the supervisor L-process. This L-process can examine
the state of the P-process and, if the attempted communication is `legal',
perform the communication and return control to the P-process. The
P-process will continue as if a normal communication had occurred.
 
There is also a `syscall' instruction which can be used by a P-process to
explicitly request some action by the supervisor.
 
Memory management
-----------------
 
When running in protected mode, all memory accesses are checked and
translated. Each P-process can access four regions of memory. The size and
base address of each region can be set, and each can have different
protections. Each area can be given permission for code to be executed from
it and for data to be written. For example an area of memory containing
code would normally be marked with execute permission but write protected.
 
All addresses generated when the processor is running in protected  mode
are logical addresses. These are translated to physical addresses by
combining the low order bits of the logical address with the high order
bits from the control register for that region. The translation and
checking is done in parallel with other address generation operations and
so imposes no overhead on memory access time.
 
The IMS T9000's memory management can be used to implement swapping of
memory to and from disk and relocation (although it does not support
page-based virtual memory). This can be used to implement most operating
system kernels. It can also be used for `stack extension'. All the
instructions which move the workspace pointer are checked for a valid
address after the operation. If it is found that the workspace address is
no longer valid then a trap occurs, the supervisor process can then
allocate more memory for the processes stack and restart it.