Introducing the INMOS IMS T9000 family
 
The INMOS IMS T9000 is the latest member of the transputer family. It is
designed to provide far higher performance and greatly improved
communications facilities.
 
INMOS has used advanced CMOS technology to integrate a 32-bit integer
processor, a 64-bit floating point processor, 16 Kbytes of cache memory, a
communications processor and four high bandwidth serial communications
links on a single IMS T9000 chip.
 
The IMS T9000 transputer excels in real-time embedded applications,
delivering exceptional single processor performance and scaleable
multiprocessor capability.
 
The IMS T9000 is binary compatible with previous transputers. It extends
the transputer range, making it easy to upgrade and complement existing
transputer systems. There is extensive, industry standard software support
for all members of the transputer family; this includes high level language
compilers, systems software (such as real time operating systems) as well
as an extensive range of development tools.
 
-----------------------------------------------------------------

Performance 
 
It is essential that any microprocessor family designed for the embedded
system market provides the required performance at low cost.
 
The transputer family includes a 16 bit processor, a 32 bit range  of fast
integer and floating point processors and now, the highest performance
member of the family, the IMS T9000. These are all designed to make it easy
to design low cost, high performance systems.
 
**  the IMS T9000 transputer boasts exceptional single processor
performance; the new superscalar CPU is capable of a peak performance of
200 MIPS and 25 MFLOPS.
 
**  the IMS T9000 offers sub-microsecond interrupt response and context
switch times, making it ideal for high performance real-time systems.
 
** the four IMS T9000 communication links provide a total of 80
Mbytes/second bidirectional bandwidth.
 
**  the interprocessor communications architecture gives scaleable
performance - the ability to increase the performance of a system by adding
more processors.
 
**  the IMS T9000 implementation makes it easy for compilers to fully
exploit the superscalar performance using a range of industry standard
programming languages.
 
**  the IMS T9000 offers supercomputer performance at an embedded systems
price.
 
-----------------------------------------------------------------

Multiprocessing
 
For applications that demand performance that single processors cannot
provide, the IMS T9000 has complete on-chip support for multiprocessing:
 
** the transputer architecture includes instruction level support for the
creation and scheduling of any number of concurrent processes
 
** the transputer instruction set includes instructions for communicating
between concurrent processes. The same instructions are used to communicate
between processes running on a single transputer and between processes
running on separate transputers.
 
**  the presence of a dedicated communications processor which operates
concurrently with the main processor, makes interprocessor communications
flexible and efficient. The integration of the communications system
on-chip makes it easy to write programs for multiprocessor systems
 
** all the IMS T9000 transputers in a system can be initialized, loaded
with code and monitored for errors through a completely independent
communications system.
 
-----------------------------------------------------------------

Communications support devices
 
The IMS T9000 transputer is complemented by a range of communications
peripherals that extend the communications capabilities of the IMS T9000.
The IMS C1XX family ensures that any size of IMS T9000 system can be
constructed, connecting first generation and second generation transputers
and providing an interface to the outside world.
 
** the IMS C104 is a complete routing switch on a single chip. The IMS C104
connects 32 links to each other via a 32 by 32 way, non-blocking crossbar
switch with sub-microseco nd latency. This allows simple, fast
communication between IMS T9000 transputers that are not directly
connected. Multiple IMS C104s can be connected together to make larger and
more complex networks, linking any number of IMS T9000 transputers, or any
other devices that use the link protocol.
 
** the IMS C100 system protocol convertor converts between the first
generation transputer links and control signals and the new IMS T9000
protocol.The IMS C100 provides an inter-networking solution for transputer
systems, allowing networks to be constructed using the optimum mix of
transputers to satisfy processing power, communication bandwidth and system
cost.
 
-----------------------------------------------------------------

Software
 
 The success of any microprocessor is determined as much by the quality  of
its software development tools as by any other feature.
 
 INMOS has over a decade of experience in developing software tools  for
transputers and for multiprocessing systems. The range of compilers and
powerful development tools support all the requirements of software
developers.
 
** instruction set compatibility with the first generation transputer
family means that the IMS T9000 transputer has inherited a significant
range of development and application software.
 
** the transputer toolset is a set of development tools for programming,
configuring and debugging mixed transputer systems.   The toolset is
available on a variety of host computers including:
 
        IBM PC
 
        NEC PC
 
        VAX
 
        Sun 3
 
        Sun 4
 
**  INMOS provides a powerful, interactive debugger for debugging programs
running on networks of transputers. This provides full source level debugging
with the ability to set breakpoints in any process and on any processor, and
then to examine the state of the stopped process as well as the low-level
state of the processor.
 
For fast time to market, and to satisfy the diverse programming
requirements of different application areas, the toolset can be used 
with a variety of industry standard compilers, all with major support 
for multiprocessing.

The IMS T9000 is supported by a range of compilers including:
 
        ANSI C
 
        C++
 
        Fortran
 
        occam
 
        Ada
 
**  system software support for the IMS T9000 reflects the requirements of the
embedded systems marketplace. A range of operating systems and real-time
kernels are available for the transputer including:
 
        C Executive
 
        VRTX
 
        CHORUS distributed Unix
 
This impressive array of development tools, industry standard compilers 
and system software satisfies the demands of the embedded systems 
market. It also ensures that the user can benefit from a significant 
reduction in the critical time to market. 
 
-----------------------------------------------------------------
Applications 
 
The transputer family provides unprecedented price/performance solutions 
for a wide range of embedded systems applications. 
 
The IMS T9000 transputer has been specifically developed to satisfy
the requirements of three segments of the embedded systems market: 
 
** the imaging market comprises applications that involve the generation,
manipulation and transmission of image data. Such applications include:
 
        Laser printers
 
        Graphics systems
 
        Image processing systems
 
        Industrial inspection systems
 
        Robotics
 
** the embedded computing market comprises applications that are run within a
computer environment and add overall performance and functionality to the
computer system. Such applications include:
 
        Application accelerators: (graphics, numerical, scientific, DTP)
 
        Disk arrays and high performance file servers
 
        Databases
 
        X terminals
 
        Supercomputers
 
        Factory automation
 
**  the embedded communications market can be segmented into two main areas
that require high performance microprocessors. These are:
 
        Networking: low cost LAN interfacing - FDDI, Ethernet;
                internetworking systems - bridges, gateways and routers.
 
        Packet switching systems.
 
The IMS T9000 transputer is highly applicable to the communications
market due to its integrated architecture combining high performance 
CPU and communication links with a packet based protocol. The IMS C104
packet routing switch has been designed to support the IMS T9000,
and is useful in a range of telecommunications switching applications.
 
The transputer family provides a range of price/performance solutions 
for all the above applications.