Support for multiprocessing
 
The requirement for processing performance in embedded systems is
continuously increasing as control algorithms become more sophisticated and
as systems become more complex. In the long term, the only solution to
these ever increasing demands for performance is the use of multiple
processors to perform parallel processing.
 
Transputers are the only microprocessors specifically designed to  tackle
the problems of building multiprocessor systems.There are advantages other
than just performance to using multiple transputers in a system; it allows
scaleable systems to be built, where more processors can be added as demand
increases, or to provide the optimum balance of price versus performance.
The communications facilities of the transputer family can also be used to
build distributed systems where, for example, the processors are located
near the equipment or components they control and use links to communicate
with other processors in the system. In addition, transputers can be used
to build high reliability, fault tolerant systems.
 
Fast interrupt response and process switch
------------------------------------------
 
In most embedded applications, there is a need for fast real time  response
(both to external interrupts and for context switching in multitasking
systems). The design of the IMS T9000 processor exploits the presence of
the two on-chip caches by having only a small number of registers in the
CPU. This means that there is little state to be saved when an interrupt or
task switch occurs, so these operations are extremely fast. These types of
operations are very efficient on the transputer because of the hardware
scheduler.
 
The register stacks are duplicated so that, when a process running  on the
IMS T9000 is interrupted, the contents of the stacks do not need to be
written to memory. This results in a sub-microsecond interrupt response.
Furthermore, the duplication of the register stacks enables floating-point
arithmetic to be used in an interrupt routine without any performance
penalty.
 
-----------------------------------------------------------------
The transputer model of concurrency
 
The model of concurrency and communication implemented by the transputer
hardware is based on the ideas of communicating sequential processes. All
the features for creating processes and communicating between them are
accessible from any high level language for the transputer and are
implemented directly by the occam programming language [2].
 
Processes and channels
----------------------
 
Each process can be regarded as a black box with internal state, which  can
communicate with other processes using communication channels. Each channel
is a point to point connection between two processes. One process always
inputs from the channel and the other always outputs to it. Communication
is synchronized: the first process ready to communicate waits until the
second is also ready, then the data is copied from the outputting process
to the inputting process and both processes continue.
 
Each process starts, performs a number of actions and then terminates.  An
action may be a set of sequential processes performed one after another, as
in a conventional programming language, or a set of parallel processes to
be performed at the same time as one another. Since a process is itself
composed of processes, some of which may be executed in parallel, a process
may contain any amount of internal concurrency, and this may change with
time as processes start and terminate. Ultimately, all processes are
constructed from three primitive processes: assignment; input and output.
 
Program structure
-----------------
 
Figure 5.1 shows an example of a system constructed from three
communicating processes. In this case there are separate processes to
handle the external hardware (the screen and keyboard) and to execute the
main, application, process. This is a modular design - only the hardware
handling processes have to be changed if the software is moved to a new
environment, the same interface (the data sent and received on channels or
`protocol') can be presented to the application process. The keyboard
handler can be interrupt driven, only being scheduled when a character is
typed, the interrupts appearing as communications. The input and output
processes can provide buffering and other filtering of the data, all of
which is invisible to the main application process, which could even be
placed on a separate processor. This use of separate processors need not
just be for performance reasons but might be done, for instance, if there
are a large number of peripheral devices which could be better handled by a
low cost 16 bit transputer. One or more high performance transputers could
then be used for the main computing processes.
 
<picture>
 
Figure 5.1  -- Processes and channels
 
Example
-------
 
The code for creating parallel processes in C is very simple. For  example,
if the three processes in the example above are external functions, then
the following code is all that is needed to run them in parallel:
 
 
#include <<stdlib.h>
#include <<channel.h>
#include <<process.h>

/*
   declare externally defined functions
*/
extern keyboard_handler (Process *p, Channel *to_app, Channel *echo);
extern screen_handler (Process *p, Channel *echo, Channel *from_app);
extern application (Process *p, Channel *to_app, Channel *from_app);

/*
   declare pointers to process and channel data structures
*/
Process *kbd_p, *scrn_p, *appn_p;
Channel *to_app, *from_app, *echo;

/*
   allocate and initialize channel data structures
*/
to_app   = ChanAlloc();
from_app = ChanAlloc();
echo     = ChanAlloc();

/*
   allocate and initialize the process data structures
*/
kbd_p  = ProcAlloc (keyboard_handler, 0, 2, to_app, echo);
scrn_p = ProcAlloc (screen_handler, 0, 2, echo, from_app);
appn_p = ProcAlloc (application, 0, 2, to_app, from_app);

/*
   now run the three processes in parallel, this call
   will return when all three processes have terminated
*/
ProcPar (kbd_p, scrn_p, appn_p, NULL);<F84> 
 
A more complete explanation of how parallel programs can be written  for
the transputer can be found in INMOS Technical Note 68, <F86><#7f>Develo
ping parallel C programs for transputers" [5].
 
The equivalent program in occam would be:
 
CHAN OF BYTE to.app, from.app, echo :
PAR
  keyboard.handler (to.app, echo)
  screen.handler (echo, from.app)
  application (to.app, from.app)
 
Multiprocessor programs
-----------------------
 
<picture>
 
Figure 5.2  -- Transputers and links
 
Every transputer implements these concepts of concurrency and
communication.  As a result, the same model can be used to program an
individual transputer or to program a network of transputers. Figure 5.2
shows a typical network of transputers connected by serial links. When a
number of processes run on an individual transputer, the processor shares
its time between the concurrent processes, and channel communication is
implemented by moving data within memory. When this programming model is
used to program a network of transputers, each transputer executes the
process, or processes, allocated to it.
 
Communication between processes on different transputers is implemented
directly by transputer links. Thus the same program can be implemented on a
variety of transputer configurations, with one configuration optimized for
cost, another for performance, or another for an appropriate balance of
cost and performance as illustrated in figure 5.3.
 
<picture>
 
Figure 5.3  -- Mapping processes onto one or several transputers
 
-----------------------------------------------------------------

Other models of concurrency
 
Although the transputer has direct support for concurrent process  which
communicate via channels, it is possible to use the same features of the
transputer to build other types of multiprocessor system or to support
different scheduling models. The IMS T9000 includes a number of
instructions for manipulating the transputer process queues; these make it
simple to write real-time kernels, exploiting the efficient task switching
of the transputer architecture. There are also instructions for ensuring
that the data in the cache and in memory are consistent. These can be very
useful when implementing a shared memory system.
 
Shared memory
-------------
 
In a shared memory system, a number of processors have some sort of  common
area of memory which they can all access. This has some advantages over the
channel communication model, especially where very large amounts of data
need to be shared or moved between processors. The transputer has hardware
and software support for shared memory systems.
 
The PMI has a set of signals for controlling access to the external  memory
interface by an external device. This is primarily intended for use with a
DMA based co-processor. It can also be used, with external arbitration
logic, to allow all of the processors in a system to access the shared
memory.
 
Alternatively, there may be a number of blocks of memory that can  be
switched into the memory map of different processors under software
control. These blocks can be used for exchanging data and passing messages
between processors. To synchronize the switching of these blocks of memory
between processors, the ideal method is to pass messages over the
transputer links; as the memory is switched to a processor's address space,
it is sent a message from the previous user of the memory to inform it that
it is now the new `owner' of the memory. This allows large amounts of data
to be moved from one processor to another but without the overhead of
copying all of it over a link.
 
In any shared memory system, the use of a cache can be a problem.  In the
IMS T9000 there are instructions for forcing changed data in the cache to
be written out to main memory and for marking data in the cache as invalid
so that it will be read from main memory. As the exchange of data is
synchronized between processors, these instructions can be used to make
sure that the correct data is in both the main memory and the cache of the
processors involved.
 
It is also possible to mark banks of external memory to be `uncacheable';
data from that area of memory will never be put in the cache. This  ensures
that a number of processors or other devices which make random reads and
writes of that memory will always get the most up to date data. In this
case there must still be some synchronization of the memory accesses to
make sure that information is not read by a processor until it has been
written; again, this synchronization can be done over the transputer links.
 
-----------------------------------------------------------------
Hardware scheduler 
 
The IMS T9000 processor includes a hardware scheduler which implements the
transputer model of concurrency. In many applications this will remove the
need for a software kernel. However, the transputers own scheduling
mechanisms can be accessed from software to provide efficient support for
the implementation of standard real-time kernels.
 
At any time, a transputer process may be:
 
   active       -      being executed
                -      on a list waiting to be executed

 inactive       -      ready to input
                -      ready to output
                -      waiting until a specified time
 
The scheduler operates in such a way that inactive processes do not
consume any processor time. The active processes waiting to be executed are
held on a list of process workspaces. This is implemented using two
registers, one of which points to the first process on the list, the other
to the last. In figure 5.4, P is executing, and Q, R and S are active,
awaiting execution.
 
A process runs until it is unable to proceed because it is waiting  to
input or output, or waiting for the timer. Whenever a process is unable to
proceed, its instruction pointer is saved in its workspace and the next
process is taken from the list. Actual process switch times are very small
as little state needs to be saved; it is not necessary for the processor to
save the evaluation stack on descheduling.
 
<picture>
 
Figure 5.4  -- Transputer process queue
 
-----------------------------------------------------------------

Interrupts, events and timers
 
As well as process scheduling and communications, the scheduling hardware
also supports simple handling of interrupts and timers. Any event that a
process might need to wait for (whether it be a communication, an interrupt
or a timeout) can be treated in the same way as a communication. For
example, an interrupt handler simply has to wait for an input from a
special channel which is mapped onto an interrupt (`Event') input. Because
inputs are synchronized, that process will not proceed until the `input'
becomes ready, i.e. until there is an interrupt.
 
This makes interrupts on the transputer very easy to use. An interrupt
handler is simply a process like any other waiting on an input from the
interrupt `channel'. This contrasts greatly with the traditional idea of an
interrupt handler as something difficult which needs to use special
instructions and be written in a very different way from other program code
(usually in assembler).
 
The IMS T9000 has four sets of pins, known as `Event' channels, which can
be used for control and synchronization purposes. Each Event channel can be
configured either as an input or an output. As inputs they can be used as
interrupts, to cause a fast processor response to a external signals. When
an Event channel is configured as an output, the process outputting to it
will be descheduled until the external device provides the necessary
handshake signal.
 
The transputer has two timers; one of which `ticks' every microsecond,  the
other ticks every 64 microseconds. The current value of the processor timer
can be read, or a process can perform a<F86> timer input in which case it
will become ready to execute when a specified time has been reached. Both
these uses of the timer are treated as inputs similar to channel
communication. If the timer is simply being read then the current timer
value is provided immediately; if the process is waiting for a particular
time, then it is descheduled until that time.
 
-----------------------------------------------------------------

Shared resources
 
The IMS T9000 also provides efficient hardware support for controlling
access to a shared resource. This could be a hardware resource (e.g. a
printer) or a piece of software running on a particular processor in a
network. Each process which wants to use the resource (a `client') can make
a request to the controlling process (the `server'). This request is done
in the form of a channel communication and can, therefore, be done across a
network by using transputer links. If the resource is available then the
requesting client is given access to it, otherwise it is put on a queue
until the resource becomes free. If multiple clients request a resource
then they are all automatically queued until it is available.
 
<picture>
 
Figure 5.5  -- Client/server model of resources
 
The resource mechanism can provide pairs of channels between the server
and the processes accessing it. This can be used, for example, to implement
remote procedure calls across a transputer system.