Network communications
 
The use of INMOS links for directly connecting transputers has already been
described. The new link protocol not only simplifies the use of links
between processors but also provides hardware support for routing messages
across a network.
 
-----------------------------------------------------------------

Message routing
 
The VCP (virtual channel processor) on the sending IMS T9000 packetizes
messages to be sent over a link and adds a header to each packet to
identify the destination process. At the receiving end, the VCP uses the
header to send the data in each packet to the intended process. These
headers can also be used for routing packets through a communication system
connecting a number of IMS T9000s together. This extends the idea of
multiple channels on a single hardware link to multiple channels through a
communications system; a communications channel can be established between
any two processes even if they are running on transputers that are not
directly connected. The header still just specifies the destination of the
packet; the programmer does not need to know how to route that message to
its destination.
 
Advantages for the programmer
-----------------------------
 
The ability to have channels between any two processes in a network  has a
number of significant advantages for the programmer. It simplifies the
description of multiprocessor systems by separating the hardware
architecture from the software configuration. The programmer doesn't need
to be concerned with the details of placing channels on links or routing
messages through the network. This removes a lot of the problems with
placing of processes on processors - the decision now can be made just on
the basis of the resources (memory size, etc.) available on each processor
without worrying about the available connectivity.
 
The programming model for networks of IMS T9000 transputers is unchanged
from that for the first generation of transputers. There is, however,
greater flexibility in configuring software. An important feature is that
the hardware and software configurations, and therefore their descriptions,
can be kept completely independent. The same hardware, and the same
description of that hardware, can be used for many different programs.
 
Routers
-------
 
The routing components in a network can be separated from the processing
elements. Messages can be passed from one processor, through any number of
routing devices, to the destination processor. This creates a temporary
path through the routing system for that message so, from the programmers
point of view, there still appears to be a single channel directly
connecting a process on one transputer with a process on another.
 
<picture>
 
Figure 7.1  -- A routing system
 
As a packet arrives on a link, the destination address must be inspected
before the outgoing link can be determined. The time before the output link
can be determined is therefore proportional to the address length. Further,
the address itself must be transmitted through the network and consumes
network bandwidth. It is therefore important that this address be as short
as possible, both to minimize latency and maximize bandwidth.
 
The router needs to arbitrate between packets which arrive at the  same
time and have to be sent out of the same link. Ideally, it should start to
output the packet as soon as possible; i.e. immediately after the output
link is determined, provided that the link is not already in use by another
packet. This keeps the latency through the network small, in contrast to a
typical packet switching network which uses a `store and forward' algorithm
in which each packet is read into a buffer, the address information is
decoded and then the packet is sent out. The delay that would be introduced
by this is unacceptable in a transputer network. Also the amount of
buffering needed would make a VLSI implementation of a large routing switch
impractical.
 
Separating routers and processors
---------------------------------
 
There are a number of advantages to keeping the communications devices  and
processing elements separate in a system. Processors can be directly
connected where appropriate, which avoids the silicon costs and extra
routing delays in a small system that doesn't need to use the routers.
Also, the design of the routing devices and processing elements can be
optimized for their different roles. For example, the routing component can
have a larger number of links than would be possible if the two devices
were integrated, because the processor already needs a large number of pins
for the memory interface and other functions. Having a routing device with
many links means that large network with a small number of routers can be
built, hence minimizing cost and latency and maximizing bandwidth. If
messages had to flow through the processor, it would increase the pin
count, power consumption and packaging costs. This approach also allows the
construction of scaleable architectures where the communications throughput
and processing power can be balanced.
 
Parallel networks
-----------------
 
Because the new link architecture allows all the virtual channels  of a
transputer to use a single link, complete, system-wide connectivity can be
provided by connecting just one link from each transputer to the routing
network. This means that the IMS T9000, with its four links, can be
connected to several different networks. This can be exploited in a number
of ways. For example, two or more networks can be used in parallel to
increase bandwidth, to provide a general purpose communications network and
an independent monitoring/debuggin g network, or as a `user' network
running in parallel with a physically separate `system' network.
 
-----------------------------------------------------------------

The IMS C104
 
An important benefit of the IMS T9000's serial links is that it is easy to
implement a full crossbar in VLSI, even with a large number of links. The
use of a crossbar allows packets to be passing through all links at the
same time, making the best possible use of the available bandwidth.
 
If the routing logic can be kept simple it can be provided for all  the
input links in the router. This avoids the need to share the hardware,
which would cause extra delays when several packets arrive at the same
time. It is also desirable to avoid the need for the large number of packet
buffers commonly used in routing systems. The use of small buffers and
simple routing hardware allows a single VLSI chip to provide efficient
routing between a large number of links.
 
Wormhole routing
----------------
 
The IMS C104 (figure 7.2) is one of a family of compatible communications
support devices for the IMS T9000. It includes a full 32 x 32 non-blocking
crossbar switch, enabling messages to be routed from any of its links to
any other link. In order to minimize latency, the switch uses `wormhole
routing' - the connection through the crossbar is set up as soon as the
header has been read. The header and the rest of the packet can start being
transmitted from the output link immediately. The path through the switch
disappears after the `end of packet/message' token has passed through. This
is illustrated in figure 7.3 . This method is simple to implement and
provides very low latency as the entire packet doesn't have to be read in
before the connection is made.
 
<picture>
 
Figure 7.2  -- Block diagram of IMS C104
 
Minimizing routing delays
-------------------------
 
The ability to start outputting a packet while it is still being input  can
significantly reduce delay, especially in lightly loaded networks. The
delay can be further minimized by keeping the headers short and by using
fast, simple hardware to determine the link to be used for output. The IMS
C104 uses a simple routing algorithm based on interval routing (described
in section 7.3.1).
 
<picture>
 
Figure 7.3  -- Packet passing through IMS C104
 
Because the route through each IMS C104 disappears as soon as the packet
has passed through and the packets from all the channels that pass through
a particular link are interleaved, a single virtual channel cannot `hog' a
route through a network. Messages will not be blocked waiting for another
message to pass through the system, they will only have to wait for one
packet.
 
Control links
-------------
 
Like the IMS T9000, the IMS C104 has two control links. One link receives
control and programming information, the other enables all the devices in a
system to be daisy-chained. The routing information for each link of each
IMS C104 is programmed, via the control link, from the controlling
processor.
 
Subsection 7.2.1 -- Using IMS T9000s with IMS C104s
 
A single IMS C104 can be used to provide full connectivity between 32 IMS
T9000s. It can also be used to connect other compatible communications
devices, for example to provide an interface to first generation
transputers via a protocol converter, or to peripheral devices via a link
adaptor. IMS C104s can also be connected together to build larger switches
connecting bigger networks of IMS T9000s.
 
The IMS C104s that the packets pass through do not need to have information
about the complete route to the destination, only which link each packet
should be sent out of at each point. Each of the IMS C104s in the network
programmed with information that determines which output link should be
used for each header value. In this way, each IMS C104 can route packets
out of whichever link will send it towards its destination.
 
Header deletion
---------------
 
An approach that simplifies the construction of networks is to provide  two
levels of header on each packet. The first header specifies the destination
transputer (actually, the output link from the routing network), this
header is removed as the packet leaves the routing system. This exposes the
second header which tells the VCP in the destination transputer which
process (actually, which virtual channel) this packet is for. To support
this, the IMS C104 can route packets of any length. Any information after
the initial header bytes used by the IMS C104 is just treated as part of
the packet, even if it is going to be interpreted as a header elsewhere in
the system.The IMS C104 can set any output link to do header deletion, i.e.
to remove the routing header from the front of a packet after it been used
to make the routing decision. The first part of the remaining data is then
treated as a header by the next device that receives the packet.
 
<picture>
 
Figure 7.4  -- Header deletion
 
As can be seen from figure 7.5, by using separate headers to identify the
destination processor and a process within that processor, the labelling of
links in a routing network is separated from the labelling of virtual
channels within each processor. For instance, if the same 2 byte header
were used to do all the routing in a network, then the virtual channels in
all the transputers would have to be uniquely labelled with a value in the
range 0 to 64K. However, by using two 1 byte headers, all the IMS T9000s
can use virtual channel numbers in the range 0 to 255. The first byte of
the header will be used by the routing system to ensure that the packets
reach the appropriate IMS T9000 before the virtual channel number is
decoded.
 
<picture>
 
Figure 7.5  -- Using header deletion to label a network
 
<picture>
 
Figure 7.6  -- Using header deletion to route through sub-networks
 
The advantages of using header deletion in a network are:
 
** It separates the headers, and therefore the routing information, for
virtual channels from those for the routing network.
 
** The labelling of the network can be done independently of the
application software running on the network.
 
** There is no limit to the number of virtual channels that can be handled
by a system.
 
Any number of headers can be added to the beginning of a packet so  that
header deletion can also be used to combine hierarchies of networks as
shown in figure 7.6. An extra header is added to route the message through
each network. The header at the front of each packet is deleted as it
leaves each network to enter a sub-network.
 
Routing control channels
------------------------
 
For very large networks, the usual method of connecting control links,  in
a chain, might introduce an undesirable delay. In this case, because of the
common virtual link protocol, an IMS C104 can be used to route the control
links to all the devices in a system more directly, as shown in figure 7.7.
 
<picture>
 
Figure 7.7  -- Routing control links through an IMS C104
 
-----------------------------------------------------------------

Routing algorithms
 
In order to route a message through a network, an algorithm is required
which is: complete (ensures that all messages arrive); deadlock free;
optimal (packets take the shortest route); scaleable (networks of any size
can be built) and simple to implement.
 
Subsection 7.3.1 -- Labelling networks
 
<picture>
 
Figure 7.8  -- Labelling a network
 
For each routing component there will be a number of destinations  which
can be reached via each of its output links. Therefore, there needs to be a
method of deciding which output link to use for each packet that arrives.
The addresses that can be reached through any link will depend on the way
the network is labelled. An obvious way of determining which destinations
are accessible from each link, is to have a lookup table associated with
all the outputs (see figure 7.8 ). In practice, this is difficult to
implement. There must be an upper bound on the lookup table size and it may
require a large number of comparisons between the header value and the
contents of the table. This is inefficient in silicon area and also
potentially slow.
 
<picture>
 
Figure 7.9  -- Interval labelling
 
However, a labelling scheme can be chosen for the network such that  each
output link has a <F86>range of node addresses that can be reached
through it. If it is then ensured that the ranges for each link are
non-overlapping, a very simple test is possible. The header just has to be
tested to see into which range, or interval, it falls and, hence, which
output link to use. For example, in figure 7.9, a header with address
<F86>n would be tested against each of the four intervals shown below:
 
The advantages of interval labelling are that: 
 
** It is `complete' - any network can be labelled.
 
** It is simple to implement in hardware - it requires little silicon area
which means it can be provided for a large number of links as well as
keeping costs and power dissipation down.
 
** Because it is simple, it is also very fast, keeping routing delays to a
minimum.
 
Subsection 7.3.2 -- Avoiding deadlock
 
Deadlock can occur in a network unless the routing algorithm is designed
to avoid it. Any program with communicating processes can also deadlock if
not designed carefully. It is important here, to distinguish between
deadlock as a property of the network and as a property of a program
running on the network. A deadlock free network cannot cause a program
to deadlock (but, of course, neither can it prevent a badly designed
program from deadlocking). An essential property of a router in a deadlock
free network is that, like a transputer or an IMS C104, it can communicate
on all of its links concurrently.
 
As a simple example consider a network of four nodes (see figure 7.10) with
one link in each direction between each node. If the routing algorithm
sends all messages clockwise and all nodes start sending to the opposite
corner at the same time, every link will become busy and the network will
deadlock. It is possible to add buffers to the network, but this will only
delay the point at which deadlock occurs. The amount of buffering needed to
avoid deadlock is dependent on the network size and the application program
running on the network.
 
<picture>
 
Figure 7.10  -- Deadlock in a network
 
In this example, deadlock can easily be avoided by modifying the routing
algorithm to send messages in opposite directions from alternate nodes. In
this case, each node will only need to send one message in each direction
at any time. In this network, buffering can be added just to smooth the
flow of data (i.e. to prevent a process having to wait to send a message
when the network is busy) but it is not needed to prevent deadlock.
 
It is possible to use interval labelling to label any network in a
deadlock free way. Many regular networks have optimal, deadlock free
routing algorithms. Examples are trees, hypercubes and grids. These
networks can then be combined, so that any network can be optimally
labelled as if constructed from these sub-networks.