Figure 3.1  -- Network of control links
 
The control links provide an independent communication network which  can
be used to load code, do hardware debugging, monitor a running system for
errors and perform diagnostic functions, both for a single IMS T9000 and a
network.
 
Because of the great flexibility of the memory interface and the
communications  system of the IMS T9000 there are a number of configuration
registers that need to be programmed. For all of these, the development
tools will program the registers using high level descriptions of the
system. For example, as noted above, there is an interactive tool for
developing configuration data for the PMI. Similarly, the communication
system is set up using high level language descriptions of the software and
hardware networks.
 
There are two ways of programming the configuration registers: by  writing
to them from a program running on the IMS T9000 itself; or via a control
link from the host system. The first method is used when the system is
booted from ROM, for example in an embedded system. The second method can
be used in a development environment or, in a multi-transputer system,
where only one processor is initialized (or `configured') from ROM and all
the others are configured via their control links from that root processor.
In both cases the IMS T9000 development tools will generate the data to be
programmed into ROM or sent to the control link of a processor.
 
There are a number of stages of initializing and loading code onto  the IMS
T9000 after it has been reset. These are known as `reset levels' and during
the initialization process, every IMS T9000 must go through each level from
complete reset, to having application code running. Each of these levels
can be done from ROM or through a control link.
 
-----------------------------------------------------------------

Loading and bootstrapping
 
The transputer can also be bootstrapped in two ways: from code received
down a link or from ROM. All INMOS development tools generate programs to
be loaded by either method as required during development or in a
production system.
 
There are a number of advantages to the ability to load code from  a link.
It greatly simplifies the development cycle - there is no need to keep
programming new EPROMs with new versions of code (or use an EPROM
emulator); it can simply be loaded down a link. It simplifies testing of
hardware - a transputer provided with the minimal essential external
signals (5 volts, clock, etc) will be guaranteed to work; there is then 16
Kbytes of on-chip RAM in which to load test code. In a multiprocessor
system, only the root processor needs to be booted from ROM - the others
can be booted down a link with code contained in that system ROM. It is
even possible to switch between ROM and link booting, in order to do field
testing and diagnose faults in an installed system.
 
-----------------------------------------------------------------

Examples
 
To show how simple it is to build systems using the IMS T9000, a few
example block diagrams are given here. In the simplest cases these are
almost complete circuit diagrams.
 
The first example (figure 3.2) is a complete working system using the IMS
T9000s internal RAM as the system memory. The processor boots from ROM
which contains the application software. This processor can communicate
with other transputers or peripherals through its data links. It can be set
to boot from ROM or from link for development and test purposes. The full16
Kbytes of on-chip RAM is available for program workspace.
 
<picture>
 
Figure 3.2  -- Complete IMS T9000 system with EPROM
 
Figure 3.3 shows how a low cost system can be built using a small amount of
SRAM. This could be combined with ROM and peripherals for a low cost
embedded application.
 
<picture>
 
Figure 3.3  -- Low cost system with 64 Kbyte of SRAM
 
The third example in figure 3.4 shows how a large amount of DRAM can be
connected to the IMS T9000 with no external logic for decoding, control
signal generation or buffering.
 
<picture>
 
Figure 3.4  -- High performance system with 8 Mbytes of DRAM.
 
The memory in each bank is enabled by separate strobe signals so all  of
the above memory types could be combined on a single IMS T9000.