Software and systems
 
INMOS provides a wide range of standard software and hardware products  to
support development for the transputer. These have been designed to enable
users to evaluate transputers and to develop systems easily and within the
shortest possible timescales.
 
Development tools include compilers for languages such as C, Fortran  and
occam as well as the software needed to test, program and debug systems
built from one or many transputers. All the special features of the
transputer are available from high level languages (either as part of the
language or as library calls).A wide range of software is also available
from third-party suppliers including compilers, such as Ada, and real-time
kernels, e.g. VRTX and C Executive.
 
INMOS also supplies a range of modular hardware products. These exploit
the ability to build very compact transputer systems (such as an IMS T805
with 4 Mbytes of memory on a board measuring approximately 2.5 cms by 9
cms) to provide a range of small, cost effective `TRansputer Modules'
(TRAMs). These modules can be mounted on a variety of motherboards, which
are available for a range of host systems. The motherboards provide an
interface to the host development system and can be connected to build
larger systems. The standard sizes and interfaces of the modules and
motherboards have been adopted by a number of third party developers to
extend the range of compatible systems products available to transputer
users.
 
INMOS will continue to support all these standards for the IMS T9000
product family, extending them where necessary to exploit the new features
of these products.
 
More details of the systems and software products currently available  for
the transputer family can be found in [5].
 
-----------------------------------------------------------------

Development software
 
INMOS has a range of development software, running on different hosts,  for
the transputer family. These tools are aimed mainly at developing code for
embedded systems, i.e. not necessarily running under the control of an
operating system. It is expected that the end products will either be
connected to a host system or will be completely self-contained units.
 
Software can be developed in standard high level languages using
cross-compilers running on a range of host machines. Programs for single
transputers can be developed using just conventional programming tools,
such as compilers and linkers. All the languages include extensive support,
in the form of run-time libraries, for concurrency and communication. It is
possible to write a program consisting of many concurrent processes
entirely in C (or any other language available for the transputer).
 
Programs written for multi-transputer systems, or programs written as many
sub-programs running in parallel on a single processor, will require the
use of extra programming tools. The transputer development system includes
tools for preparing a program for execution on a parallel processing system
and for debugging such systems. These tools include `configuration' tools
which are used for describing the hardware, mapping processes to
transputers and setting up the communications channels. It is possible to
boot and load a network with code from the host development system, or from
a ROM connected to one of the transputers in the network. Programs can
communicate with a `server' on the host system to get access to host
facilities such as i/o. In addition there are tools for debugging a program
running on a network of transputers. An outline of some of these transputer
specific tools is given below.
 
All of the programming tools are available for all members of the
transputer family and, where appropriate, are used in the same way and
provide the same functions for all processor types.
 
Subsection 9.1.1 -- Configuration tools
 
In discussing IMS T9000 transputer systems, the word `configuration' is
used in two senses. The first is when an IMS T9000 transputer, or an IMS
C104, is initialized - at this time a number of internal `configuration'
registers have to be written to program the PMI, the VCP and other
subsystems. The process of preparing a program for loading onto a
transputer network is also referred to as `configuration' (and the software
tools used are known as `configurers'). In this description of the
development process, the word `configuration' is reserved for the latter
meaning of software configuration; the setting up of the hardware will be
called `initialization'.
 
The configuration tools are used to build programs consisting of a  number
of processes or sub-programs running in parallel on one or more
transputers. Input files are used to describe the hardware, the software
and a mapping of the software onto the hardware. From these, the
configuration tools produce the files which are used to initialize and load
the transputer network.
 
Hardware description
--------------------
 
The hardware is described using a Network Description Language (NDL).  For
each transputer in the system, this specifies the processor type, the
amount and types of memory and peripheral devices. It also describes the
routing network used, if any, and how the data and control links of all the
devices in the system are connected.
 
The configuration tools use this description to program the PMI and  VCP
registers of the IMS T9000 and to label the links of any IMS C104s used.
The information in this file is also used to create the bootable version of
a program to run on the network.
 
If certain simple rules are followed in the construction and labelling  of
networks, then the tools can check the descriptions for errors and deadlock
freedom. The NDL description can also be checked against the actual
hardware.
 
Software description
--------------------
 
The NDL file for a particular system will normally be provided by  the
hardware vendor or designer. The programmers using the system only need to
include a reference to the NDL file in the software configuration file. The
NDL description exports the names of the processors and routes in the
network for use in the software and mapping description.
 
The software description has to specify the object code files for  each
process in the system and the procedure interface (parameters and their
types). Optionally, other language dependent attributes can be defined. For
example, the size of stack and heap areas for a C program can be specified.
The software description must also specify the way that any communication
channels are used between processes.
 
Mapping software to hardware
----------------------------
 
A mapping of software (processes) onto hardware (transputers) must  also be
given. The mapping can be as simple as a series of statements of the form:
`place process on processor' for each process in the program. Any number of
processes can be placed on each processor, allowing a program to be
initially tested on a single processor before the multi-processor version
is tried. The configuration tools automatically work out the mapping of
channels onto virtual links. If necessary, for example to access the host
system or a particular piece of hardware, the programmer can explicitly map
channels onto links or routes through the network.
 
Configuration languages
-----------------------
 
To provide a degree of flexibility for the user, there are two `dialects'
of configuration language: a C-like one and an occam-style one. These
perform identical functions but each has a different syntax, loosely based
on these languages. These configuration languages are used for describing
the structure of the software and how it is mapped onto the hardware.
 
Types of networks
-----------------
 
The INMOS development tools support development of programs for:
 
Networks consisting of IMS T9000 transputers only (`non-routed' networks).
 
Networks consisting of IMS T9000 transputers and IMS C104 routers (`routed'
networks).
 
Networks consisting of any other transputer types.
 
The tools do not directly support arbitrary, mixed networks of IMS T9000
transputers and first generation devices. However, it is possible to
connect the two types of networks, via an IMS C100, although the code for
the two sub-networks has to be developed separately. The two networks can
then be loaded from the host, via a common route.
 
In the case of non-routed networks (of any transputer type) the
configuration tools automatically add routing software to the program to
provide any communications required between processors which are not
directly connected.
 
A network of IMS T9000 transputers can be loaded with code compiled for an
IMS T805 or an IMS T9000. This allows users to write programs for the IMS
T9000 even if the compiler used is only available for the IMS T805. It also
means that existing, compiled code can be run on an IMS T9000 system.
 
Subsection 9.1.2 -- Initializing and loading a network
 
Transputer systems can be bootstrapped in two ways; either from ROM  or
from link. The initialization and initial code loading are done via the
control link. This initial boot code then loads the main application code
from the data links of the processor.
 
Levels of initialization
------------------------
 
The initialization and loading of code for the IMS T9000 are done in a
number of stages. The various levels of initialization can be done either
by code running on an IMS T9000 booted from ROM, or from the host system
via the control link. In a network, different processors may be initialized
to different levels from ROM with the later stages being done via the
control link.
 
Booting a system from link
--------------------------
 
The `boot from link' option is normally used during program development  or
whenever a system needs to be able to run different programs at different
times.
 
In order to load a network from a host system, connections to a single
control link and a single data link are required. This data link normally
goes directly to an IMS T9000, the rest of the network being loaded via
this processor. The development tools generate data files which are used to
do all the initialization and loading of code onto the network.
 
Booting a system from ROM
-------------------------
 
The development tools can produce a number of different types of ROM.
These range in function from performing the (partial) initialization of a
single IMS T9000, to booting an entire system.
 
When booting a system completely from ROM, it is possible to have  a single
ROM on one processor. This root processor boots from the ROM and then
initializes and loads the rest of the network via links; all other
transputers in the network being set to boot from link.
 
Subsection 9.1.3 -- Host servers
 
A server is a program that runs on the host machine to give software,
running on an attached transputer system, access to various host facilities
such as i/o and disk storage. The server typically loads the executable
code onto the transputer network via a link interface. It then waits for
requests and data to be sent by the transputer program. These requests
generally come from the run-time library, when the program makes calls to
standard input and output functions (e.g. printf() in C).
 
The server allows the development tools running on the host to control  the
target transputer system in order to reset the system, do any
initialization needed and then load a bootable program file. Software
running on the host can also use the server to access the transputer system
for testing and debugging.
 
The nature of the connection from the host to the transputer system
depends on the type of the host system, but generally provides access to
transputer links either directly, via a link adaptor on the host bus, or
through some other standard communications system such as Ethernet. In many
cases the server software includes a device driver, which handles the low
level details of the hardware interface, plus a set of functions to access
the link through the device driver.
 
Subsection 9.1.4 -- Debugging
 
INMOS provides an interactive symbolic debugger for debugging programs
running on networks of transputers. This supports source level debugging of
programs which consist of a number of parallel processes running on any
number of processors. The user can set breakpoints, inspect the state of
processes (including expression evaluation, modification of variables,
backtracing procedure calls, etc) as well as examining the low level state
of each transputer in the system. A very useful feature is the ability to
`jump' down a communication channel between two processes - this allows the
state of two communicating processes to be examined.
 
The debugger is currently being developed further to make it more  powerful
and easier to use. Some of the features that will be added are:
 
** Window based user interface.
 
** List all processes running in the network.
 
** Stop processes to examine their state.
 
** Source level single stepping.
 
** History tracing (e.g. keeping track of communications events).
 
** Variable watchpointing.
 
Subsection 9.1.5 -- IMS T805 emulation
 
An IMS T9000 can be booted from a ROM which performs all initialization and
then executes a loader program. The loader then waits for code to arrive on
any of the data links. This emulates the behavior of the IMS T805 which,
after reset, waits for bootstrap code to arrive on a link. With the
addition of an IMS C100 to do protocol conversion, this provides the
ability to plug an IMS T9000 directly into an existing transputer network
and program it as if it were an IMS T805.
 
Because the IMS T9000 is binary compatible with, and has the same
programming model as, previous transputers the programmer can use existing
development tools, source code, libraries and programming techniques.
 
This compatibility also makes it easy for systems companies to port
existing software, such as real-time kernels, compilers and so on, that
have already been developed for the current transputer range. This enables
an IMS T9000 specific version of these products to be developed very
quickly. Additional work can then be done, if necessary, to extend the
product to make use of new features of the IMS T9000.
 
-----------------------------------------------------------------

Iq Systems products
 
There is already a wide range of TRAMs and motherboards designed for  the
first generation of transputers. This includes modules with transputers
plus various amounts and types of memory, through to various industry
standard interfaces such as SCSI and GPIB. There is a complementary range
of motherboards interfacing to hosts such as PC and Sun.
 
These TRAMs and industry standard motherboards make it easy to develop,
prototype and build multiprocessor systems, based on the transputer family.
 
Subsection 9.2.1 -- IMS T9000 products
 
To support the IMS T9000, a number of products compatible with the existing
TRAM definition are being designed. In the longer term a new module
standard is being defined to exploit the faster links and other features of
the IMS T9000. In addition the approach to systems design using the IMS
T9000 will be somewhat different because of the facilities provided by the
virtual links.
 
The objectives of the new range of systems products are:
 
** No jumpers or switches on boards - the user can simply plug together
modules to build a system and start using it.
 
** No cables for interconnection within a system - all link
interconnections via a backplane and IMS C104s.
 
** Flexible but fixed network topology - this will be chosen to provide
complete connection between all transputers in a system with minimal
latency.
 
** Provision of 3.3V for new high speed, low power components.
 
** Ability to use existing TRAMs where appropriate.
 
** Ability to build fault tolerant and `live insertion' systems.
 
** Standard interfaces inside and outside the box.
 
The opportunity will be taken to increase the modularity of the systems
components, and to improve the design mechanically and provide better
support for peripheral interface connections. To allow flexible
interconnection of boards and modules, a backplane architecture is being
defined to enable the construction of routed and non-routed systems. These
and other changes are being made based on experience and customer feedback.
 
The new standards will embrace modules, boards and system interconnections.
This includes the construction and interconnection of scaleable systems
with small (1-10) through medium (up to 64) to large (>256) numbers of
processors.
 
The new module standard will include the provision of a ROM which  may be
used to provide configuration data for the memory interface, etc. In some
cases the processor might boot from this ROM as well. The ROM will also be
used to store useful information about the board, such as the module type,
serial number, vendor, memory size and speed, and information about other
peripheral devices.
 
The new backplanes will be based on metric standards and will provide  a
standard backplane interface. This will probably follow the board and
connector formats defined by the Futurebus Plus standard.
 
The transputer links are, naturally, used for connecting between
transputers  on a single board or within a system. There is also a need for
longer connections between systems, for example to support interfacing
between a target system and the development host. Two standards are being
defined; an electrical connection for distances up to about 10 meters, and
a low cost optical fiber interconnect for longer distances.
 
Compatible development products
-------------------------------
 
Initially, INMOS will provide a TRAM compatible with current standards  but
containing an IMS T9000. To provide compatibility this will have an IMS
C100 to convert the links and control signals. The IMS T9000 will boot from
ROM so it can be initialized and then be ready to load code down a data
link; it will then appear just like a very fast IMS T805.
 
This TRAM can be used in an existing development environment to do  initial
evaluation of code running on the IMS T9000. The program running on this
TRAM can communicate but will obviously not have the IMS T9000 advantages
of very high speed links and the virtual channel mechanism.
 
A similar product will be developed, allowing the IMS T9000 to be used in
an existing development system, but providing direct connection of the IMS
T9000 links. This will enable more realistic multiple IMS T9000 development
to be undertaken.
 
IMS T9000 specific products
---------------------------
 
INMOS is developing a range of IMS T9000 modules based on the new standard.
These will range from simple `compute only' modules, with a transputer and
memory, through to interface modules. These will provide access to
standards such as SCSI, FDDI, etc. Motherboards for these modules will also
be supplied, both to the new standard and for popular host computers, such
as the IBM PC.
 
Host interfaces
---------------
 
There is a need to provide a new type of interface to efficiently  support
communication between a host system and a program running on an IMS T9000
system.
 
The existence of multiple virtual links into a network can be exploited  to
simplify the way that software on the transputer accesses host services.
This can also be used to provide all transputers with access to the host.
The handling of virtual channels on the host could be implemented in
hardware for highest performance or software for greatest flexibility and
lowest cost. The choice depends on the capabilities of the particular host
hardware and operating system, as well as user requirements. For example,
the data transfer speed required will be different in a development
situation and an accelerator.
 
The requirements for connecting into the data link network and the  control
network are quite different. The data links will typically have a
relatively small number of virtual channels connecting to the host, but
will require very high data rates (especially if the IMS T9000 system is
being used an an accelerator or co-processor). There are potentially a very
large number of virtual control links but these can run at a lower data
rate.