The IMS T9000 transputer
 
The IMS T9000 is the latest member in the transputer family of high
performance microprocessors. It is part of a broad range of 16 and 32 bit
microprocessors with compatible instructions sets and interfaces. As well
as providing high performance processing, they are designed to be simple to
use and enable the construction of low cost systems. Transputers include
functions to enable multitasking on a single processor and the building of
multiprocessor systems.
 
-----------------------------------------------------------------

Overview
 
<picture>
 
Figure 2.1  -- Block diagram of IMS T9000
 
The IMS T9000 integrates a high performance central processing unit (CPU),
a 16 Kbyte cache, communications system and other support functions on a
single chip. The main functional blocks of the IMS T9000 are shown in
figure 2.1. The function of each of these is outlined below, more details
will be found in the following sections.
 
Processor
---------
 
The IMS T9000 CPU contains a 32 bit arithmetic and logic unit (ALU) and a
64 bit floating point unit ( FPU). The FPU operates on 32 and 64 bit
floating point numbers as specified by the IEEE 754 standard. The CPU also
includes instructions for byte and half word operations. The CPU uses 32
bit linear addressing and can address up to 4 Gbytes of memory.
 
The IMS T9000 is binary compatible with previous transputers. In particular
it implements the same instruction set as the IMS T805 [1] with many
additions.
 
The instruction set is designed for efficient execution of compiled  code
and there is a wide range of language compilers available for the
transputer including a Plum-Hall validated ANSI C compiler, a validated Ada
compiler and Fortran, occam and C++ compilers. These are complemented by a
full set of software tools for developing and debugging programs for single
transputers and networks of transputers. In addition there are a number of
system level software products, such as real time kernels and distributed
operating systems.
 
The transputer includes a hardware kernel for scheduling processes  and
performing communications. These operations are directly supported in the
instruction set.
 
The IMS T9000 can run code in protected mode. In this mode all memory
accesses are made through a memory management unit which checks and
translates addresses before using them to address the memory system.
Further, only a subset of the full instruction set may be executed,
preventing protected code from executing privileged instructions.
 
There is improved support for error handling over earlier transputers;
errors can be trapped and handled independently for each process in
addition to the global error handling provided previously.
 
Hierarchical memory system
--------------------------
 
The IMS T9000 includes a 16 Kbyte unified cache to provide single cycle
access to instructions and data. The cache provides a peak bandwidth of 200
Mwords/s. The CPU also includes another small cache for the most frequently
used local variables of a program which provides another 150 Mwords/s of
memory bandwidth.
 
The external memory interface is highly programmable, allowing large
memory systems, containing different types of devices, to be built with
little or no external logic. There are four independent sets of memory
control signals simplifying the use of different device types in the same
system. The memory can interface to 8, 16, 32 or 64 bit wide devices. The
maximum data transfer rate across the memory interface is 50 Mwords/s.
 
Communications system
---------------------
 
An important issue in multiprocessor system design is the communications
architecture. To achieve efficiency and ease of use, communications must be
properly integrated into the entire processor architecture.
 
The transputer hardware and instruction set provides simple and efficient
communications between processes and between processors. Both internal and
external communications are handled identically, using the same source code
and machine instructions.
 
To support interprocessor communications, there is a complete
communications  subsystem on chip. This includes four 100 Mbits/s
full-duplex, serial communication links each with its own pair of direct
memory access (DMA) channels. The links can be directly connected between
transputers with no external buffering or other glue logic. The use of
serial links simplifies routing of links on a circuit boards and the
interconnection of boards in a system.  A communications processor, which
manages all link communications, operates concurrently with the main CPU so
that data transfers do not adversely affect CPU operation.
 
Two additional links are provided for system control and monitoring.
Initialization and booting of the processor can optionally be done through
these links.
 
The communications subsystem also includes four `Event' channels.  As well
as acting as interrupt inputs, these can be used, as inputs or outputs, for
more general synchronization and signalling.
 
Multiple internal buses
-----------------------
 
To support the high degree of concurrent operation on the IMS T9000, and to
maintain the high internal data rates required, there are four sets of 32
bit address and data buses internally. These provide multi-por t access to
the on-chip cache from the various functional units of the IMS T9000.
 
System services
---------------
 
The system services section provides all the general facilities necessary
for the operation of the transputer. This includes the power and ground
connections, and the clock input (5 MHz). Other important connections are a
capacitor, which is required for the on-chip phase locked loops which
generate all the internal high frequency clocks, and the processor speed
select pins which can be used to select the frequency of the internal
clocks (up to the maximum speed for a particular device). There is also a
reset input - however, as the IMS T9000 includes on-chip power-on reset
circuitry, external reset logic may not be required in an embedded control
application.
 
-----------------------------------------------------------------
 The transputer architecture
 
An important design decision was that transputers should be programmed  in
a high level language. The instruction set has, therefore, been designed
for simple and efficient compilation.The instructions are all of the same
format and chosen to give a compact representation of the operations most
frequently occurring in programs.
 
The CPU of the IMS T9000 contains three registers (Areg, Breg and Creg)
used for expression evaluation, which form a hardware stack. Loading a
value into the stack pushes Breg into Creg, and Areg into Breg, before
loading Areg. Storing a value from Areg pops Br eg into Areg, and Creg into
Breg. Similarly, the FPU includes a three register floating-point
evaluation stack. When values are loaded onto, or stored from, the stack
the floating-point registers push and pop in the same way as the Areg ,
Breg and Creg registers. Analysis of a large number of programs, shows that
3 registers provides an effective balance between code compactness and
implementation complexity.
 
<picture>
 
Figure 2.2  -- Processor registers and memory
 
The transputer has three other registers used when executing code.  These
are:
 
** The instruction pointer which points to the next instruction to be
executed.
 
** The workspace pointer which points to an area of store where local
variables are kept. This area is also used as a stack for procedure calls,
etc.
 
** The operand register which is used in the formation of instruction
operands.
 
The addresses of floating-point values are formed on the CPU stack, and
values are transferred between the addressed memory locations and the FPU
stack under the control of the CPU.
 
Most transputer functions use the contents of these stacks, and most
instructions reference the stacks implicitly. For example the add
instruction adds the top two values in the CPU stack, leaving the result on
the top of the stack. The use of a stack reduces the need for instructions
to specify the location of their operands which reduces the size of
instructions and hence of compiled code.
 
-----------------------------------------------------------------

Support for concurrent processes
 
Most computers have the ability to effectively run several user tasks  or
processes concurrently. These processes are created and scheduled by the
host operating system. The operating system kernel provides the ability for
processes to communicate with the operating system and with each other.
 
Every transputer includes a hardware kernel with the ability to execute
many software processes at the same time, to create new processes rapidly,
and to perform communication between processes within a transputer and
between processes on different transputers. All of these operations are
integrated into the hardware and instruction set of the transputer and are
very efficient. Further details of the transputers scheduling mechanism
will be found in section 5.
 
-----------------------------------------------------------------

Pipelined, superscalar implementation
 
To increase the execution rate of the transputer instruction set,  the IMS
T9000 is able to issue several instructions per cycle. A superscalar
micro-architecture was designed which implements the same high level
architecture and instruction set as the IMS T805 but with much higher
performance.
 
Some recent implementations of pipelined and superscalar microprocessors
have required very careful programming to obtain the claimed performance.
They require that instructions are presented to the pipeline in a sequence
that will keep the processor busy. This makes developing effective
compilers very difficult, often forcing programmers to resort to assembly
code to achieve the required performance. This puts the burden of arranging
the correct sequencing of instructions on the programmer, adding to the
development time and hence costs of a product.
 
<picture>

Figure 2.3  -- Block diagram of grouper and pipeline
 
The details of the IMS T9000 pipeline are transparent to the programmer.
The processor appears to be the simple transputer architecture described
above and straightforward code written for that programming model will get
nearly the best performance out of the processor. An optimising compiler
for the IMS T9000 can, of course, generate more efficient code if the
details of the internal architecture are taken into account.
 
The pipeline
------------
 
Instructions are executed in a five stage pipeline: the first can  fetch
two local variables; the second can perform two address calculations, for
accessing non-local or subscripted variables; the third stage can load two
non-local variables; the next can perform an ALU or FPU operation; and the
final stage can do a conditional jump or write.
 
A conventional pipeline is designed to allow several instructions  to be
executed simultaneously; different parts of each instruction being handled
in different stages of the pipeline. In order to allow multiple
instructions to be issued per cycle (as well as multiple instructions being
executed in each cycle) the IMS T9000 does not simply send a sequence of
instructions through the pipeline but has hardware which assembles groups
of instructions from the instruction stream. These groups are chosen to
make the best use of the available hardware and one group can be sent
through the pipeline every cycle. Instructions are put into groups in the
order that they arrive at the CPU; dependencies within the group are
handled automatically by the pipeline.
 
The grouper can be thought of as a hardware optimizer; it recognizes
commonly occurring code sequences that the processor can execute
effectively. The design of the grouping mechanism and the pipeline is based
on analysis of the code typically generated by high level language
compilers.
 
An IMS T9000 running at 50 MHz can execute code compiled for the IMS T805
typically10 times faster than a 20 MHz IMS T805. This means that existing
development tools and software can be used to generate code for the IMS
T9000. It also means that only a modest amount of work is required to
modify compilers to produce code optimized for the IMS T9000.
 
Grouping of instructions
------------------------
 
The grouping of instructions takes advantage of the high degree of
concurrency and multiple buses in the processor. For example, both caches
are multi-ported and can each support two reads by the CPU simultaneously.
This allows two <F86>load local instructions to go into one group, and the
group could also contain two sets of instructions to calculate addresses
and fetch non-local variables. These could all be combined with an
arithmetic operation such as add. More details of the transputer
instruction set can be found in [3].
 
As an example of how the grouper works, consider the assignment and
expression evaluation shown below. The code produced is shown along with
the number of the pipeline stages in which it is executed.
 
                ldl   j         load local variable j
                ldl   b         load base address of array b
                wsub            calculate address of b[j]
                ldnl 15         load value of element b[j+15]

                ldl   k
                ldl   c
                wsub
                ldnl  7         load value of c[k+7]
                add             add two values on top of stack

                ldl   i
                ldl   a
                wsub
                stnl  1         store into a[i+1]
 
This code sequence will be executed as three groups (i.e. in 3 cycles)  as
shown below. The exact contents of each group will depend on the code which
precedes and follows this. The first group might contain other instructions
from earlier in the instruction stream.

First group                     ldl, ldl, wsub, ldnl

Second group                    ldl, ldl, wsub, ldnl, add
 
third group                     ldl, ldl, wsub, stnl
 
Since the processor can fetch one word, containing four bytes of
instructions  and data, in each cycle it is possible to achieve a
continuous execution rate of four instructions per cycle (200 MIPS).
However, if any of the instructions require more than one cycle to execute,
then the instruction fetch mechanism can continue to fetch instructions so
that larger groups can be built up. Up to 8 instructions can be put into
one group and there may be five groups in the pipeline at any time.
 
Improvements over IMS T805
--------------------------
 
In addition to executing several instructions each cycle, the number  of
cycles required to perform many arithmetic and logical operations has been
reduced from previous transputers by adding extra hardware. This, combined
with the faster clock speed and new micro-architecture, means a ten-fold
increase in speed over the IMS T805.
 
In addition there is improved support for error handling, and protecting
code and data from the errant behavior of a program. The IMS T9000 provides
better access to the transputers scheduling mechanism, making it easier to
implement software kernels for a particular processing model.
 
-----------------------------------------------------------------

Hierarchical memory system
 
<picture>
 
Figure 2.4  -- IMS T9000 hierarchical memory system
 
The IMS T9000 has a complete, hierarchical memory system providing fast and
efficient access to data and instructions. There are two separate caches on
chip, a general purpose unified (code and data) cache and a small cache for
local variables.
 
These caches can provide fast, multi-ported access to data because they are
on chip. They also reduce the number and frequency of accesses to external
memory, allowing lower cost, slower devices to be used without degrading
performance. Finally, because the majority of external memory accesses will
be cache refills (and therefore multiple word reads and writes) fast memory
access methods, such as page mode, can be used.
 
Subsection 2.5.1 -- Main cache
 
The main cache consists of four independent banks, each containing  256
lines. Each line holds data from four consecutive words (16 bytes) in
memory. An access can be made to every bank on every cycle which, with the
multiple internal buses, means there is a very high bandwidth between the
cache and different functional units within the IMS T9000.
 
<picture>
 
Figure 2.5  -- Diagram of four banks of cache
 
The four cache banks are accessed by a number of different functional
units in the IMS T9000, some of these units have multiple ports into the
cache. To allow four simultaneous reads and writes to take place in each
cycle, there are four sets of address and data buses. An arbitrator
controls access from the various functional units to the cache banks.
 
Cache operation
---------------
 
Each of the four banks is addressed by a quarter of the memory space.  This
division of the address space is done using bits 4 and 5 of the address,
the bottom four bits are used to select a byte within a line. Each line
consists of: 16 bytes of RAM for the data; 26 bits of associative memory
which holds the address of this line of data; and two control bits to
indicate if the line is valid and if it has been modified since it was read
in (is `dirty'). When a memory access is made, the address is checked
against the contents of the appropriate bank. If the address is present
(and the line is valid) then the access can go ahead, reading or writing
the data in a single cycle.
 
A cache refill engine ensures that there is always one empty line
available. Then, if a requested address is not in the cache (a `cache
miss'), the four words containing the data are read from memory into the
empty line. The refill engine then has to ensure that a new empty line is
created. It does this by choosing a line at random and, if the data has
been modified since it was read into the cache, writing it out to memory.
The line is then marked as invalid, i.e. empty and available for use. This
is known as `early write-back' as it writes the chosen line out to memory
before a cache miss occurs.
 
The reading and writing of cache lines takes advantage of any fast  memory
access methods that are available (e.g. 64 bit wide accesses or page mode
DRAM).
 
Use as on-chip RAM
------------------
 
At reset, the cache behaves as 16 Kbytes of normal RAM, enabling the  IMS
T9000 to be used with no external memory. There may be many applications
where a number of transputers are used, each requiring little or no
external memory - used in this way the IMS T9000 provides extremely high
performance (single cycle memory reads and writes) combined with extremely
low cost (possibly no external components except a clock). Starting up in
this mode provides compatibility with earlier transputers which have a
fixed amount of on-chip RAM. It also makes it possible to test the hardware
of a new transputer system as it is known that there is 16 Kbytes of
working RAM which can be used by test software.
 
During the initialization of the IMS T9000 the cache may be programmed to
behave as 16 Kbytes of cache, as 16 Kbytes of RAM, or as half cache and
half RAM. This can be very useful when certain data or code, e.g. an
interrupt handler, must be accessed quickly and in a more deterministic way
than a cache provides. The remaining 8 Kbytes of cache will be large enough
to achieve high performance.
 
Subsection 2.5.2 -- Workspace cache
 
The workspace cache can hold a copy of the first 32 words of procedure
stack and workspace. It is triple ported, allowing two reads and a write in
every cycle. The workspace cache allows local data to be accessed without
going outside the CPU, effectively giving zero cycle access and reducing
the load on the main cache and external memory. It also means that the
pipeline can do four data reads (as well as an instruction fetch) in each
cycle: 2 from the local cache and 2 from the main cache.
 
Because local variables can be accessed quickly, they can be read  in the
first stage of the pipeline and can then be used for non-local address
calculations in the next stage. The workspace cache is write-thro ugh;
whenever data is written into the local cache it is also written to the
main cache. This means there is no overhead for flushing the cache on
interrupt or context switch.
 
The workspace cache is part of the processor pipeline and, in many  ways,
it is equivalent to the general purpose register set found on other
microprocessors, providing fast access to frequently used data. To make use
of this architecture, the INMOS ANSI C compiler recognizes the `register'
keyword and places those variables lower in the function's workspace so
they are more likely to be cached.
 
Cache operation
---------------
 
The cache is organized as a 32 word circular buffer and is addressed  using
the bottom five bits of the workspace pointer. As the workspace pointer
moves up and down, it rolls around the cache. When the workspace pointer is
moved down, on a procedure call for instance, the locations that `roll
into' the cache are marked as invalid and become valid as they are read or
written. The first time a variable is read, it is copied from the main
cache (and, of course, fetched from main memory if it is not in the main
cache). Lines are marked as invalid when they `roll out' of the cache as
the workspace pointer is moved up (e.g. on a return from a procedure call).
On a context switch or interrupt, the entire contents of the cache are
marked as invalid.
 
This is illustrated in figure 2.6, where the state of the workspace cache
during a procedure call and return sequence is shown. Before the call, the
locations in the workspace cache above the workspace pointer which have
been read or written by the program contain valid data. After the call, the
workspace pointer moves down - initially the locations which are above the
workspace pointer are invalid; as they are accessed by the program they are
filled with data and marked as valid. When the procedure returns, the
locations which it used will be marked as invalid. As long as the workspace
of the called procedure is less than 32 words, some of the workspace of the
calling procedure will still be valid after the return. Nested procedure
calls, or calls of procedures with a large workspace requirement will cause
the workspace pointer to wrap around so that some of the data at the top of
the program workspace is no longer in the cache.
 
<picture>
 
Figure 2.6  -- Effects of call and return on workspace cache
 
As the cache is a circular buffer, moving the workspace pointer by  32 or
more will cause the pointer into the cache to wrap right round, marking
every line as invalid.