A Processor to Generate
C code to Communicate Using
occam Protocols


	In the course of writing various special servers to support
communications between the host machine and a transputer board it is common to
use some sort of user defined protocol between the host CPU and the transputer.
The occam compiler will provide all of the error and consistency checking
between the SC's but there has been no automated way of ensuring that when the
host CPU communicates with the transputer that it will be using the same tag
constants or the same number and type of variables in the I/O list.  This
document describes the capabilities and usage of a utility which will take
occam source code and generate from it C source code which will aid the
programmer in writing C code for the host CPU to use when communicating with
the transputer.

	The name of the utility is cprot.  It is used from the host environment
by typing

	cprot [[-m2|-t[2|4|8]]] [-h2|-h4] [-l] protocol.occ

Execution parameters are as follows:

	-m2	This parameter tells the processor to generate C code which is
		for communicating with an M212 transputer

	-t2	This parameter specifies that the host CPU is communicating
		with a T212 transputer.

	-t4	This parameter causes the processor to generate C code to 
		communicate with a T414 transputer.

	-t8	The processor will generate code for communicating with a T800 
		transputer when this parameter is used.  Please note that the
		parameters -m2, -t2, -t4 and -t8 are mutually exclusive.  If
		none of these parameters are specified -t8 will be assumed.

	-h2	This parameter causes the generation of code for a host CPU
		which has two bytes per word.

	-h4	This parameter causes the generation of code for a host CPU
		which has four bytes per word.  Notice that the parameters -h2
		and -h4 are mutually exclusive.  If both parameters are omitted
		then four bytes per word are assumed.

	-l	This parameter controls whether the code generated is for
		little endian or big endian hosts.  Intel processors are little
		endian architectures.  That is, the address of a word is the
		address of the least significant byte in the word (this is the
		convention the entire transputer family uses).  Motorola
		processors are big endian architectures.  If this parameter is
		omitted "big endian" is assumed.

	When using the processor only protocol declarations and VAL statements
should be in the file being processed.  Also the occam code which will be
communicating with the host should have been fully compiled and linked before
trying to use the host processor to generate C code for the host.  The
processor assumes that the occam code being processed is valid!

	The processor will generate two files.  The first is a C header file
containing the #define statements to declare the constants and tags found in
the occam source code file for the C code that will be running on the host. 
The second file contains C source code for function routines that can be used
to read and write data via the link adaptor.  The names of the two output files
will be generated from the name of the input file.  If the input file has the
name protocol.occ the header file will have the name protocol.h and the source
code file will have the name protocol.c.  If the occam file contains the
following code

	VAL patch.size IS 16:
	PROTOCOL draw
	  CASE
	    clear.screen
	    draw.patch; INT; INT; INT; [patch.size][patch.size]BYTE
	:

The processor would generate a header file with the following definitions:

	#define patch_size      ((tint)16)
	#define clear_screen    ((unsigned char)0)
	#define draw_patch      ((unsigned char)1)

Notice that all of the occam names which have dots ('.') in them have been
changed.  C uses dots as operators to access subfields in programmer defined
data types.  So the processor replaces dots with the underscore character
('_').  The C source code that the processor would generate would look
something like the following:

	#include "protocol.h"   /* where protocol.occ was the name
	                         * of the occam file with the
	                         * declarations in it.
       				 */

	void    read_clear_screen(LinkId, Timeout)
		int	LinkId, Timeout;
	{
	/* This routine needs no code in it since this part of the
	 * protocol only has a tag associated with it!
	 */
	}

	void    read_draw_patch(LinkId, Timeout, a, b, c, d)
		int	LinkId, Timeout;
	        tint    *a;
	        tint    *b;
	        tint    *c;
	        tbyte   d[patch_size][patch_size];
	{
	/* Some C code which magically reads the correct things from
	 * the link and stores it in the correct places!
	 */
	        .
	        .
	        .
	}

	void    write_clear_screen(LinkId, Timeout)
		int	LinkId, Timeout;
	{
	        byte_to_link(LinkId, Timeout, clear_screen);
	}

	void    write_draw_patch(LinkId, Timeout, a, b, c, d)
		int	LinkId, Timeout;
	        tint    a;
		tint    b;
	        tint    c;
	        tbyte   d[patch_size][patch_size];
	{
	        byte_to_link(LinkId, Timeout, draw_patch);
	        /* Some C code which magically writes the appropriate
 	         * data up the link to the transputer.
	         */
	        .
	        .
	        .
	}

The meaning of the data type tint will be dependent upon the execution
parameters which specify the transputer type and the host word size.  It will
always be the C data type with the same size as INT for the transputer being
communicated with.  Also available are the types tint16, tint32, tint64, tbool,
treal32, treal64 and tbyte.

	For the user code to use the C code for a read the user should emulate
the occam input code

		CHAN OF draw:
		INT x.position, y.position, size:
		[patch.size][patch.size]BYTE patch:
		input ? CASE
		  clear.screen
		    ...  Clear the screen
		  draw.patch; x.position; y.position; size; patch
		    ...  Draw patch

with C code like the following:

		tbyte   tag;
		tint    xpos, ypos, size;
		tbyte   patch[patch_size][patch_size];
		.
		.
		.
		switch (tag=tbyte_from_link(LinkId, Timeout)) {
		 case clear_screen:
		        read_clear_screen(LinkId, Timeout);
		        /* Clear the screen */
		        .
		        .
		        .
		        break;
		 case draw_patch:
		        read_draw_patch(LinkId, Timeout, &xpos, &ypos, &size,
			 patch);
		        /* Draw the patch */
		        .
		        .
		        .
		        break;
		 default:
		        /* Some sort of error handling code */
		        .
		        .
		        .
		}

	When writing your C server code you will need two special variables. 
They are LinkId and Timeout.  These variables are required by the LINK.C
interface supplied by Inmos with the D705B version of the Transputer Tool Set. 
They must be passed to the I/O routines which implement the protocols.  The
link you wish to use for I/O must be opened and closed via the LINK.C interface
routines.  The source code for the LINK.C interface is included with the D705B
software and its object code must be linked in for the protocol functions to
work.  For more information about the LINK.C interface refer to your D705B
documentation.