INTRODUCTION
------------

This document describes two tools which are provided to enable EPROM
programming with the toolset language systems (e.g.  the occam toolset).
Equivalent facilities are provided with the Transputer Development
System.

The tools provided are an interactive means to generate parameters for
the memory interface configuration, and a tool to transform code files
into EPROM images.

The memory interface configuration tool produces timing data from memory
interface parameters.  The parameters you supply can be in a file or in
response to the tool's prompt.  The tool produces a graph of the strobe
timings and a file containing the parameters which can be used to
program a ROM.  There is also an interactive interface to this tool
which allows the user to experiment with configurations.  Graphical
output is in ASCII characters or in PostScript; the tool is provided in
source so that it can be modified for other graphic standards if
necessary.

The EPROM tool reformats the output from a language system into Intel
Hex format ready for loading into EPROM programmers.  This tool is
provided in source so that it can be adapted for use with other EPROM
programmer formats.

The later chapters of the manual contain notes written by the author of
the software which will be of interest to anyone wishing to modify the
source versions of the tools which are provided.



 Distribution

The root directory contains the following subdirectories:


src: The C source of the main tools
bin:    Executable binaries of the tools
lib:    Sources and binaries of loaders


These directories should be copied onto your machine, and the bin
directory added to the search path.

EXTERNAL MEMORY INTERFACE PROGRAM
---------------------------------


 Introduction

The IMS T414 and IMS T800 transputers have a configurable memory
interface which allows a variety of types of memory device to be
connected using few extra components.  The interfaces on the two
processors are identical so `T414' will be used to mean `T414 or T800'
in this chapter.

The external memory interface configuration program produces timing
diagrams for potential configurations of the memory interface and warns
of possible errors in the design.  It indicates whether one of the
T414's preset configurations would be suitable, or whether it would be
necessary to use an externally programmed configuration.  Should an
external configuration be necessary, the program can produce a table of
data describing it.  This table is read by another program in the
transputer toolset, the EPROM hex program (q.v.), which includes them in
a ROM for the target system.

This chapter describes how to use the program and outlines its
capabilities.  Familiarity with the memory interface of the T414 and the
properties of memory devices will be assumed: relevant information will
be found in the device data sheets and in Inmos Technical Note 9,
Designing with the IMS T414 and IMS T800 Memory Interface .  Section
1 of this note is particularly useful, although the prospective designer
should read the entire document.

Output from the program is either plain ASCII files containing timing
data or PostScript format files containing waveform diagrams.  These
formats were chosen so that the results of the program could be easily
included in reports or other documentation.  The program is capable of
saving and reloading configurations to allow for design over an extended
period and for comparison of different configurations.

The current version of the program does not include the full
characterisation data for the processors.  When these are added, the
timing information generated by the program may change slightly.


 Operation

The program is called iemi .  It has no command line options, control
being entirely interactive.

Output from the program is organised into several page s.  As each page
is shown, the user has the option of selecting another page for display
by keying in its number.  The information displayed and options
available on each page will now be described.


 Page 0

This page acts as an index to the others.  It shows the title of each
page and permits the selection of one of them.  Other options are also
available, only from this page:

 S: save pages to a file

The program prompts for the name of a file to which the data will be
written.  If the file already exists, the opportunity to abandon the
save is given.  Output is in plain ASCII format with a form feed (FF)
character after each page.  It includes full timing information and a
representation of the timing diagrams for read and write cycles.  An
error is reported if the data could not be saved.

L: load previously saved configuration

A filename is prompted for, and the configuration saved in that file is
read in.  The program expects a file in the same format as that in which
it saves configurations.  This means that if the file has been modified
in any way since saving, the operation in not guaranteed to work.
Checks are made on the file, but these are not exhaustive.  In
particular, if any part of page 1 is changed in the saved file, the load
may well fail.

If loading does not succeed because the file has a bad format, the
current configuration is reset to standard configuration 31.  If loading
fails because the file could not be found or could not be opened for
reading, the load is abandoned without losing the current configuration.

P: generate PostScript file

The program prompts for a filename.  If the file already exists, the
user may abandon the operation.  The program writes to the file a
program in the PostScript page description language to draw the timing
diagrams for the chosen memory interface configuration.  The waveforms
shown are the same as those which can be seen by selecting pages 4 and
5.

The file produced fully conforms to the PostScript structuring
conventions, allowing it to be processed by other programs.  The diagram
is designed to fit lengthways on an A4 page, and is suitable for
inclusion in technical notes and reports.  The file can be sent directly
to an Apple LaserWriter or other PostScript output device.


Q: quit

Selection of this option exits the program.

 Page 1

This page shows the input parameters to the program.  It is from these
parameters that the program computes the timing information and the
waveforms.  The parameters can be adjusted and the effects of these
changes seen.

The first parameter is the device type.  Knowledge of this enables the
program to deduce the time taken for a half cycle of the signal
   ProcClockOut : this is Tm , the basic unit of time of the memory
interface.  The value of Tm for a ClockIn frequency of 5MHz is shown
next.  The number of wait states in the current configuration is
computed from the other parameters and displayed.  The number of periods
   Tm which each Tstate T1-T6 lasts is then given, followed by the names
and, where applicable, programmed durations of the strobes
   notMemS0 - notMemS4 , notMemRd and notMemWrB .  The strobes each have
two names: one which can be up to 9 characters in length, and one
consisting of just one character.  The short names are used in the
timing information on pages 2 and 3, while the long names are used to
label the waveforms on pages 4 and 5, and in the PostScript output.  The
signal names are initialised to sensible defaults.

The refresh period is given as a number of ClockIn periods (18, 36, 54,
or 72) or as Refresh Off if zero is selected.  The chosen write mode is
shown as Early or Late as appropriate.  The MemWait input may be
connected to one of the strobes S2-S4; alternatively it may be connected
to a simulated external wait state generator that causes
   MemWait to become inactive (low) a set number of Tstates after the
start of T2.  Note that this mode is not supported directly by the T414;
in a final design, a circuit would have to be built to perform this
function.  The former case is shown by the strobe name, while the latter
is shown just as the chosen delay.

If the current connection of MemWait causes the signal to become
inactive just as ProcClockOut is falling during T4, a warning that there
is a hazard of a wait race condition is given.  This is because
   MemWait is sampled on the falling edge of ProcClockOut -- and if the
signal is changing while being sampled, the result is undefined.

If the currently set configuration happens to correspond exactly to one
of the preset configurations of the T414, the program reports the fact.

When the page is displayed, the user has the option to select a new page
by entering its number, or entering C to change one of the parameters.
In the latter case, a prompt appears requesting selection of the
parameter to be changed.  The possibilities are as follows:

D: device type

A menu of the available devices appears, and the user is invited to
select one.  As elsewhere, just pressing RETURN at this point leaves the
current selection unchanged.


T1...T6: Tstate period

The length of the chosen Tstate can be changed.  Legal values are in the
range 1...4 Tm periods.


S0...S4: strobe names and durations

The durations and names of the strobes can be altered.  Note that S0 is
a fixed strobe, so its duration cannot be changed.  The duration of a
strobe can be 0...31 Tm periods.  If the value for S1 is set to zero,
then notMemS1 stays high throughout the cycle; if the value for S2, S3
or S4 is set to zero, then the strobe is low for the duration of the
cycle.


RS: read strobe names

The names for the read strobe can be altered.


WS: write strobe names

The names for the write strobe can be altered.  Note that because the
four byte write strobes have the same timing, only one is considered.


R: refresh period

The refresh period can be set to one cycle every 18, 36, 54 or 72
   ClockIn periods, or to 0 to switch refresh off.


W: wait connection

The wait connection can be set to S2, S3, S4, or to a number in the
range 0...60.  The latter choice corresponds to the connection of
   MemWait to a wait state generator that holds the signal high for the
given number of periods Tm after the start of T2.


WM: write mode

The write mode can be set to early or late to suit the type of memory
being used.


C: reset to standard configuration

The parameters can all be reset to those for one of the built in
configurations of the T414.  Valid configuration numbers are 0...11 and
31.

 Page 2

This page shows general timing information for the interface, such as
delays between various strobes and required access times of the memory
devices to be used.  The total cycle time is given in nanoseconds and in
processor clock cycles.  No special options are available from this
page.

 Page 3

This page gives timing information of special interest to designers
working with dynamic memory, including various access times and the time
for 256 refresh cycles.  Thus can the designer ensure that the
requirements of the memory devices to be used are met.  Again, no
special options are available.

 Page 4

Page 4 shows graphically the timing for a memory read cycle.  The
   Tstates and strobes are labelled, and bus activity is shown.  The
point where data are latched into the processor is also indicated.  If
the cycle is too long to fit horizontally on the screen, it may be
scrolled left and right using the L and R options.  The displayed area
moves by about 15 characters each time these options are used.

 Page 5

Page 5 shows the waveforms for a memory write cycle.  Scrolling to the
left or right is permitted in the same way as on page 4.  The read and
write cycle diagrams are combined when the PostScript output is
produced.

 Page 6

This page gives a configuration table for the current configuration.
This is a listing of the data which have to be placed in a ROM situated
at the top of the transputer's memory map in order to achieve the
desired configuration.  The table consists of 36 words of data, but only
the least significant bit in each is used.  The address and contents are
given for each location.  Note that if page 1 indicates that the
configuration is one of the transputer's preset ones, there will be no
need for a ROM; configuration can be achieved by connecting the
   MemConfig pin of the device to one of the address/data lines.

EPROM HEX PROGRAM
-----------------



 Introduction

It is easiest to boot a transputer network from a host transputer using
one of its links.  But if there is no host computer, you can boot a
transputer from EPROM.

Only one transputer needs to be booted this way because, once booted, a
transputer can boot its neighbours with a program which is stored in the
same EPROM.

This chapter describes several different ways an application can be
booted and explains how they work.


 Your application in EPROM

Unless your application has extremely tight demands for space
efficiency, the simple case described first will be sufficient.  If you
use this simple case, most of the design has already been done by INMOS.
The sections following describe more detail and how the system can be
adapted to specific needs.


 Network program (simple case)

In this case the program is loaded by a root transputer which has a
EPROM.  The network can consist of one or more processors.

You need only supply file containing a bootable program as produced by
INMOS tools.  The structure of this file is discussed later as is the
function of the precompiled multi-board loader procedure which comes
with the toolset.  The operation of the multi-board loader is similar to
the one described in Loading transputer networks which is Technical
note 34, available from INMOS.

Make sure that the program will run on the network you are using before
you blow the program into EPROM.  This can normally be verified by
booting the program file through the link on the root transputer from
the development host.

To invoke the EPROM software type, for instance:


ieprom /s /p netprog.btr /r 16 /o image


The program will report the storage requirements; the RAM size 0 bytes
indicates that the save on analyse option is disabled.  The data for the
EPROM programmer appears in a file called image .


 An example of the simple case

My network consists of only one processor with four 32Kbyte EPROMS and a
T414 and does not need memory configuration.  I want to make the error
light flash.  My EPROM programmer accepts Intel Hex format but cannot
separate the bytes.

The program is written in occam, developed on an IBM pc:


PROC wiggle.error ()
  VAL delay IS 5000000:
  TIMER time:
  SEQ
    GUY
      CLRHALTERR
    PRI PAR
      WHILE TRUE
        INT now:
        SEQ
          GUY
            TESTERR   --tests and clears error
          time ? now
          time ? AFTER (now PLUS delay)
          GUY
            SETERR
          time ? now
          time ? AFTER (now PLUS delay)
      SKIP
:

It is compiled with the e, and w options.

The configuration program is as follows:


#USE "wiggler.c4u"
PROCESSOR 0 T4
  wiggle.error ()


And the EPROM image file was created with this command:


ieprom /r128 /i /s   /p wiggle.btr /b


Notice that the input program file has the .btr extension.  The tool
prompts for start addresses of the blocks which is always zero, and the
start addresses of the blocks in EPROM which is also always zero.  The
byte selectors are done one at a time (0, 1, 2, 3).


 Main procedure only

To program the machine in this way you must use a language system which
can generate a file which is equivalent to occam toolset files with
.rxx extensions.  This file is specified to the /s option of the EPROM
image creation program.  No /p option is specified -- the transputer can
only execute what has been written into this procedure.

The advantage of programming a special main process over a single
processor network is that it makes more optimal use of both EPROM and
RAM.  No copy of code is made, compared with the network load method
which copies the program into RAM before execution.

The disadvantage is that the EPROM is often slower access memory than
RAM which may have an impact on the speed of execution.


 Transputer monitor

Conventional microprocessors' development boards have monitors which are
used to bootstrap the processor.  This is often used with RS232 for
programs to be downloaded from a host or a more sophisticated monitor
may enable programs to boot from a secondary storage device under the
control of the microprocessor.  You can use the transputer in this way
as well, and an example of a monitor for some INMOS boards is provided
with the release.  In practice, it is generally more convenient to use a
link adaptor interface with a host computer.

The transputer monitor is a case of single processor applications which
were discussed in the previous section.


 Network program (general case)

The way that the EPROM software is provided means that you have complete
flexibility, even if you are specifying both a loader procedure and a
network program

The occasions when a new loader procedure is needed are not likely to be
met very often.  Either the network program would be in a different
format to the one currently used by INMOS, or the loader needed to
continue execution after all packets had been sent to the network.


 EPROM tool input files

The program can take three files as input.  They are:


  1) a main procedure
  2) a PROGRAM
  3) the output from the external memory interface configuration program


Of these only the main procedure must be specified, the others are
optional.


 The main procedure

This will either be the final application or a loader program.  In
either case it will be of the xx format as described in the occam2
toolset manual .  The program will read this file and extract from it
the target transputer type and the version number of the file.  An error
is flagged if an the version number is incompatible with the processor
type.


 The PROGRAM file

The PROGRAM file is only required when a loader program is being used,
and must be of the .btr type.  Its contents are copied without
modification to the final EPROM for use by the loader.  The file should
therefore be of a format compatible with the chosen loader program.  No
checks are made on the validity of this file.


 The memory configuration file

This file is produced using the save command of the external memory
interface configuration program .  The chapter describing that program
should be consulted for further information.

The configuration file is scanned to find the configuration table, which
is then inserted into the EPROM at the correct point for the processor
to read it during initialisation.  If no configuration file is
specified, a blank configuration is stored in the EPROM.  If a
configuration file is specified and the processor type given in the main
procedure file is one without a configurable memory interface, an
appropriate warning message will be printed and the file ignored; no
configuration data will be inserted in the EPROM.

It is important that the file produced by the external memory interface
program not be edited before it is used.  Some checks are made on the
file but these are not exhaustive -- the use of an edited file can
produce unexpected results.


 EPROM tool output files

The program can produce output in a form readable by humans or in a form
readable by EPROM programmers.  The supported formats are described
below.  Whichever form is used, it is sometimes necessary to output the
data in blocks.  This block mode operation is also discussed.


Note that there is no output for unused areas of the EPROM -- if the
buffer in the EPROM programmer is not initialised before loading the
files produced by this program into it, unused areas of the EPROM will
be filled with random data.  Although the operation of the bootstrap
code and loader programs will not be affected by the presence of random
data, these areas of the EPROM cannot subsequently be programmed without
erasing the whole device.


 Hex dump

This simple format is intended to be used to check the output from the
program.  The dump consists of rows of 16 bytes each, prefixed by the
address of the initial byte of each row.  The format contains no
characters other than the hexadecimal digits, the space character and
newlines.


 Intel hex format

This is a commonly used protocol for EPROM programming equipment.  A
sequence of data records is sent.  Each record contains a few bytes of
information, a start address and a checksum.  In addition, a special
record marks the end of a transmission.  Since the format only supports
16-bit addresses, longer addresses are truncated and a warning message
printed.  Records produced by this program contain at most 16 bytes
each.


 Intel extended hex format

This format, also known as Intel 86 format, is similar to Intel hex, but
adds another type of record.  The new type 02 record is used to specify
addresses of more than 16 bits.  The type 02 record contains a 16-bit
field giving a segment base offset .  This value is shifted left four
places and added to subsequent addresses.  This mimics the operation of
the segment registers on the Intel 8086 range of microprocessors.  The
segment base offset value persists until the next type 02 record occurs.
This format therefore allows addresses up to 20 bits in length.  Again,
longer addresses will be truncated by the program with a printed warning
to that effect.  The program minimises the number of type 02 records
inserted in its output.


 Block mode operation

 Block mode must be used if either the programmer cannot separate
out the data bytes in the way described above, or the programmer's
buffer in not large enough to hold all the data for the EPROMs together.

 Block mode disabled

If the /b option is not specified on the command line, the program will
write its output to the file specified by the command line /o option.
Once the data file is written, the program exits.  In this simple mode,
addresses in the output file range from zero up to the specified total
EPROM size.  Bytes are output in the order in which they should appear
in the transputer's address space.  If separation of the bytes for
several EPROMs is required, it must be done by the EPROM programmer.

 Block mode enabled

If the /b option was given on the command line, then a wider range of
possibilities is available.  Data blocks are output each into a separate
file.  For each block, the start and end addresses in the EPROM space
can be given, together with the corresponding output address.  Further,
if a set of byte-wide EPROMs is being produced to go side-by-side in a
system, it is possible to generate the data required for each byte in
the word separately.

First of all, the program asks for the offset into the EPROMs of the
start of the block to be written.  This offset can be any value greater
than or equal to zero and less than the total EPROM size entered
earlier.  Then the offset into the EPROMs of the end of the block is
prompted for: this can be any value less than or equal to the total
EPROM size and greater than or equal to the start offset.  If the end
offset is equal to the start offset, no data will be output.  Between
them, these two values specify the section of code that is to be
included in this block.

The option is then given to output just the data for one particular byte
in each word, or for the entire word.  If a byte number is entered, then
only bytes whose address has that number as its byte selector will be
output.  This function is useful when preparing side-by-side EPROMs.

The name of the file to which this block of data is to be written is
then prompted for; any filename specified with the command line /o
option is ignored.  The block of data is the written out.

The diagram below illustrates a rather atypical case where a total of
64K of EPROM is being attached to a T414 32-bit processor using sixteen
4Kx8 EPROMs.  Sixteen separate files are to be produced using block
mode.  It is assumed that the programmer has only four kilobytes of
buffer space, starting at address 8K.  This means that the output
address must be 8K for each file, so addresses in the file will range
from 8K to 12K.  The parameters for the sixteen blocks are thus as
follows:


block   start offset  end offset   output   byte
number  into EPROMs   into EPROMs  address  number
  0      0K             16K         8K       0
  1      0K             16K         8K       1
  2      0K             16K         8K       2
  3      0K             16K         8K       3
  4      16K            32K         8K       0
  5      16K            32K         8K       1
  6      16K            32K         8K       2
  7      16K            32K         8K       3
  8      32K            48K         8K       0
  9      32K            48K         8K       1
 10      32K            48K         8K       2
 11      32K            48K         8K       3
 12      48K            64K         8K       0
 13      48K            64K         8K       1
 14      48K            64K         8K       2
 15      48K            64K         8K       3



 Calling the EPROM tool

 The program is controlled both by command line options and
interactively.  The program is called ieprom and its command line
options are as follows:

 tabular ll
   -s<filename> specify main procedure file name
   -p<filename> specify PROGRAM file name
   -c<filename> specify configuration file name
   -o<filename> specify output filename
   -r<decimal number> specify EPROM size in kilobytes
   -m<decimal number> specify target machine RAM size in kilobytes
  and enable ``copy for analyse''
   -h produce simple hex dump
   -i use Intel hex output format
   -e use Intel extended hex output format
   -b enable block mode (see below)
   -l load program only and remain silent
 tabular

The program then proceeds to construct the EPROM contents.  If one of
the files which is read is found to have a bad format, an error message
is produced and the program terminates.  Otherwise, the program reports
the required amounts of EPROM and RAM.

At this stage the program has, in effect, created an image of the data
that are to appear in the target transputer's memory space in an
internal buffer.  The task now is to transfer the contents of this
buffer into EPROMs for the target system.  Since most EPROM devices are
only eight bits wide, and the transputer data bus is 16 or 32 bits wide,
several EPROMs will be required ``side-by-side''.  In a 16-bit system,
one of the two EPROMs will contain the data bytes at even addresses,
while the other contains those at odd addresses.  In a 32-bit system,
each of the four EPROMs will contain every fourth byte.  This means that
at some stage the data will have to be separated out into the two or
four blocks required, one for each byte in the word size of the
destination system.  Many EPROM programmers can perform this task, but
it may be found more convenient to use separation features, especially
if the programmer's buffer is not large enough to hold the contents of
all the EPROMs simultaneously.

Note that the T212 16-bit transputer has a memory interface with a
``byte access'' mode that allows the use of byte-wide memory devices.
This mode is discussed in detail in the data sheet for the device and
allows the use of a single EPROM for booting the transputer.  If this
mode is being used, separating out the bytes for the EPROM will not be
necessary.


 Typical T414 system example

Suppose that it is required to produce four 32Kx8 EPROMs in a T414
transputer system.  The T414 will require the four 8-bit EPROMs to
provide the data on its 32-bit bus.  Since a separate EPROM is needed
for each byte, block mode will have to be used.  The total EPROM size
would be entered as 128K (32K multiplied by 4), and four blocks would be
generated.  Each would have a start offset of zero and an end offset of
128K, and the byte numbers would be specified successively as 0, 1, 2
and 3.  This would produce four files, one for each EPROM.  The EPROM
programmed from the file generated with byte number 0 would ultimately
be connected to data lines 0 to 7, while that with byte number 3 would
be connected to data lines 24 to 31.  The output address that should be
used will depend on the EPROM programmer being employed.


 Typical T212 system example

Suppose a single 16Kx8 EPROM is to be programmed for a T212 system using
its ``byte access'' mode mentioned above.  This can be done directly
without the -b flag, entering a total EPROM size of 16K.  The output
file generated will have addresses in the range 0 to 16K.

Alternatively, if a different range of output addresses is required, or
if the programmer cannot handle 64K of data in one pass, block mode must
be used.  When prompted for the byte number, the user should just press
 RETURN to allow all bytes to be included in the EPROM.


 Repeating options

If a large number of EPROMs is to be programmed on a regular basis, and
block mode is being used, it will be found convenient to automate the
production of the data files.  The simplest way to achieve this is,
during one run, to make a note of the entries made to the program and
subsequently construct a file containing them, one entry per line.  When
the program is next run, the interactive input stream can be redirected
to come from this file.



 Initialising the transputer state

The action of the processor on reset, when booting from EPROM, is to
start executing instructions from the location (MOSTPOS INT) - 1: this
is
  7FFFFFFE for 32-bit machines and 7FFE for 16-bit machines.  A
backwards jump to the bootstrap code is inserted by the program at this
address.  The bootstrap code first preserves then initialises the
processor state (including the links, the event channel, the timers and
the process queues).

If the copy for analyse option is requested (see below), it also makes a
copy of the bottom 600 bytes of RAM at the top of the RAM area.  This is
done to preserve information which might be useful in determining the
state of the processor before it was analysed, but likely to be
overwritten by a loader procedure.


 Calling the main procedure

After the processor is initialised, the main procedure is called.  It
should be declared as follows:

 PROC INMOS.ENTRY.POINT (INT entry.point,
                        [60]BYTE buffer,
                        VAL[600]BYTE memory.copy,
                        VAL[]BYTE program.buffer)
  SEQ
    ... the code
:

The parameters are:

   entry.point The main procedure should store the offset from MostNeg
INT of successor process (see below) here.  This entry address will also
be the initial value of the workspace pointer for the successor process.

   buffer This array contains the state of the transputer before it was
reset; this information will be useful in debugging programs.  When
retyped into an array of INT s, the contents of buffer are as follows:

   buffer[ 0]: value of Iptr
   buffer[ 1]: value of Wptr
   buffer[ 2]: low priority process queue front pointer
   buffer[ 3]: low priority process queue back pointer
   buffer[ 4]: high priority process queue front pointer
   buffer[ 5]: high priority process queue back pointer
   buffer[ 6]: error state
   buffer[ 7]: value of halt-on-error flag
   buffer[ 8]: floating point unit error state (T800 only)
   buffer[ 9]: low priority timer value
   buffer[10]: high priority timer value
   buffer[11]: undefined
   buffer[12]: address of the array memory.copy
   buffer[13]: undefined
   buffer[14]: undefined

   memory.copy The 600 bytes of information copied from low memory.

   program.buffer The area in the EPROM where the data bytes from the
PROGRAM file are stored.  If (SIZE program.buffer) is zero, then there
is no PROGRAM file in the EPROM.  This happens when no program file is
specified to the EPROM program on its command line.

If the procedure returns, it should leave the entry address and initial
workspace pointer for the successor process in entry.point .  If no
successor process is to be run, the procedure should not return.



 Program

There are several ways in which the EPROM hex program can be used,
depending on whether a PROGRAM file is supplied or not.

If no PROGRAM file is given, then it is assumed that the main procedure
file contains the final application program that the system is to run.
This mode is intended for those single processor systems where
performance will not be adversely affected by the fact that the
transputer is running its program from EPROM.  In this case, the
procedure should be written so that it either loops indefinitely or all
processes STOP ; if it ever returns, subsequent operation of the system
is undefined.

In some systems, accesses to EPROM are significantly slower than those
to RAM; in such cases, it can be worthwhile copying the application code
from EPROM into RAM before executing it.  This can be achieved by
supplying the application code as a PROGRAM file to the EPROM hex
program.  The procedure should then be a suitable loader program which
performs the copy from EPROM to RAM and sets up the entry address for
the loaded code as described above.

The EPROM that the program helps to produce may be connected to the
master transputer of a network and be required to boot that network
along its links.  In this case, the procedure should be the multiboard
loader and the PROGRAM file should include the code to run on each
processor in the system.

If present, the network program will be distributed by the main
procedure described above.  Once the loader has distributed all of the
network it exits leaving the processor with the EPROMs as the root
processor of the configuration as described in user manual of the
language system being used.


 Memory configuration

The memory configuration file is optional.  Transputers have a number of
selectable standard external memory interfaces.  For transputers with an
external memory interface 32 bits wide, this interface can also be
programmed to a non-standard set-up.  In these cases the memory
interface is read by the transputer after reset from specified addresses
in its address range.  These addresses are within the area covered by an
EPROM which can be used to boot a transputer.

If a memory configuration is required in the EPROM, the configuration
must be provided to the EPROM hex program as a series of address/value
pairs.  In the case of T4 transputers there must be 36 pairs.


EXTERNAL MEMORY INTERFACE PROGRAM NOTES
---------------------------------------


 Introduction

It will be found useful when reading the following to refer to a listing
of the program, to copies of the IMS T414 or T800 data sheets, to Inmos
Technical Note 9, ``Designing with the IMS T414 and IMS T800 Memory
Interface'' by Tony Gore and David Cormie, and possibly to a treatise on
the PostScript page description language.


 Defined constants

The value SX is the horizontal size of the output device, less 1.  Thus
it will take the value 79 for an 80 column screen.  It should be changed
if the program is to be used with other output devices.

The value noval is a flag value used in the tables of timing information
where a value is not meaningful: the value will be printed as a single
dash character by the function vtos() .

   tscale is the scaling used in time calculations.  Since these
calculations are performed in integers, inaccuracies may result if the
nanosecond were used as the basic unit of time.  tscale is normally set
to 10, so that all timings are held internally in units of 0.1
nanoseconds.  This affects the tolerance table and cycle time variables.

The remaining definitions are for indices into the arrays outmin[] ,
   outmax[] , start[] and stop[] .


 Variables

   outmax[] stores the values shown in the `max' column of the timing
tables.

   outmin[] stores the values shown in the `min' column of the timing
tables.

   start[] holds the number of the Tstate (counting from 0) where each
of the strobes goes low.

   stop[] holds the number of the Tstate (counting from 0) where each of
the strobes goes high.  If both start[] and stop[] are equal to the
variable endstate , then that strobe never becomes active.

   nst is the number Tstates shown in a display on page 4 or 5.

   chst is the number of screen characters occupied horizontally by one
   Tstate .

   leftst if the number of the leftmost Tstate shown.  This is changed
by scrolling operations.

   rtst if the number of the rightmost Tstate shown.  This is also
changed by scrolling operations.

   pst is the number of points (1 point = 1/72 inch) occupied
horizontally by one Tstate in the PostScript output.

The tolerance tables, which have the same names as in the occam version,
give characterisation data for the devices, such as the possible skew of
various signals.  The units of time used are dependent on the value of
tscale (see section 1).


   dtm[] is half the device cycle time, indexed by device number, again
measured in the time units given by tscale .

   waitrace is a flag which is true when there is a wait race hazard.

   waitperiods is the total number of wait states added to the memory
cycle.

   extrastate is true if the entire cycle lasts an odd number of periods
   Tm , and an extra state needs to be added at the end.

   endstate is the total memory cycle time in periods Tm .

   a is an instance of a struct config and holds the current
configuration.  The structure has the following members:

   type , the number for the device type;
   t[] , the duration of the Tstate s;
   s[] , the duration of each strobe;
   rfsh , the interval between refresh cycles in periods of ClockIn , or
zero if refresh is switched off;
   wait , the connection of the wait strobe: -1 corresponds to
   notMemS2 , -2 to notMemS3 and -3 to notMemS4 .  Nonnegative values
correspond to connection to a wait state generator extending MemWait by
the given number of Tm periods after the start of T2;
   wrm , the write mode, which is 0 for early write and 1 for late;
   snam[][] , the long names for the strobes;
   sch[] , the short names for the strobes.  Strobes are stored in the
order S0...S4, Read, Write.

   snam[][] holds the default long names for the strobes.

   sch[] holds the default short names for the strobes.

   conf holds the number of the current configuration, if it is one of
the preset configurations of the memory interface, and -1 otherwise.

   prefig...[] hold the parameters for the preset interface
configurations, and are indexed by the configuration number.

   dnam[] holds the names of the devices known to the program, indexed
by the device number 0...8.

   fp points to the FILE structure for the stream to which output is
currently directed.  This is normally stdout , but is changed when a
save operation is taking place.

   page holds the number of the currently displayed page.

   qf is a flag set to true when the user requests that the program
exit.

   s[] and t[] are string areas used for many purposes.

   pagedraw[] is an array of pointers to functions which handle the
drawing of each page, indexed by page number.

   pagekey[] is an array of pointers to functions to handle user input
after each page.  Note that there are only four distinct keyboard
handlers, as some are shared between several pages.


 Functions

   main() initialises the current configuration's strobe names to their
defaults, and all the elements of arrays outmin[] and outmax[] to
   noval .  It resets the horizontal scroll position for pages 4 and 5,
   leftst , to zero, the device type to `T414-17' and the wait
connection to 0, so that no wait states will be generated.  By calling
conftoa() it resets all the parameters to the defaults for configuration
31 (the declaration of conf initialises it to 31).  The call to
   compute() then works out all the timing information and other
variables so that they are in a consistent state.
   fp is set to stdout so that output is to the user's console, and,
while the user has not chosen to quit the program,
   pagedraw[page] and pagekey[page] are called alternately.

   page0() simply prints the index page, calling centre() where
appropriate.  Note that all printing is done with fprintf(fp,...) so
that when fp points to a real file, the output is saved.

   page1() draws the parameter page.  It includes a call to race() to
check the wait race condition and print a warning message if necessary.
Note that the EMI clock period is scaled by tscale so that the value
appears as a time in nanoseconds.  Data for the page are extracted from
the structure a and other variables.  It is important that these be made
consistent by calling compute() and atoconf() before this function.

   page2() draws the general timing page.  It calls vtos() to render a
time value either as a number, or as a `-' character if the value is
equal to noval .

   page3() draws the dynamic memory timing page.  Again vtos() is called
to print the time values.

   page4() calls waves() with parameter 0, so drawing the read cycle
timing.

   page5() also calls waves() but with parameter 1, so it draws the
write cycle timing.  Pages 4 and 5 have been integrated in this way
because of the large amount of information which they have in common.

   page6() prints the configuration table by calling ctlin() for each
line.  The data to go into the table are taken entirely from the
structure a .

   key0() prompts the user for a page number, or to select one of the
other options available from page 0.  If `S' is entered, save() is
called; if `L' is entered, load() is called, and if `P' is entered,
dops() is called to generate a PostScript file.

   key1() is called after page 1 is printed, and allows selection of a
new page, or `C' to change one of the displayed parameters.  In the
latter case, changes() is called.

   key2() allows only selection of a new page number.

   key4() allows selection of a new page, and left and right scrolling
by entering `L' or `R'.  scrolll() and scrollr() are called as
appropriate.

   centre() prints the string passed to it in the middle of the line.
It uses the defined constant SX to determine the required indentation.

   save() writes out all the pages to a file.  The name is prompted for,
and an attempt is made to open the file for reading.  If this succeeds,
the file is closed and the user is asked if it is to be overwritten.
The user can then abandon the save operation.  The file is then opened
for writing, and fp set to its file handle.  Each of the pagedraw[]
routines is then called in turn, and a form feed character printed after
each.  Finally, the file is closed, and fp restored to stdout .

   conftoa() takes a configuration number in conf and loads the
structure
   a with the values appropriate to it, by looking up the values in the
prefig...[] arrays.  No change is made if conf is set to -1.

   atoconf() takes a configuration in the structure a and checks to see
if it corresponds exactly to any of the preset ones.  If it does, conf
is set to the relevant value, and otherwise to -1.

   changes() allows the user to alter any of the available parameters.
It prints a list of the parameters that can be adjusted, and prompts for
one of them.  In each case the old value is printed, and the user
invited to enter a new value.  If no entry is made, the current value is
left unchanged.  All inputs are checked for validity.  After the changes
are made to the values in a , atoconf() is called to check whether the
new configuration is actually the same as one of the preset ones, and
set conf appropriately.  Finally compute() is called to make all the
variables consistent.

   vtos() converts a number into a string, returning `-' if the number
was equal to noval .  The resulting string is padded to 5 characters so
that the tables of data in pages 2 and 3 are aligned in columns.

   ctlin() is used to print one line of the configuration table for page
6.  It is called with five arguments, v , w , x , y and z .  On each
line two table entries are printed; each consists of an address and a
digit that is either 1 or 0.  v is the line number, from which
   ctlin() computes the addresses to be printed.  The two digits printed
are bit x of w and bit z of y .

   compute() works out both the activity on all the strobes and the
timing parameters.  It stores the Tstate where each strobe goes low in
the array start[] , and the Tstate where it returns high in the array
stop[] .  It simulates the wait state generator if necessary, and
computes the values of waitperiods , waitrace , extrastate and
   endstate .  It checks whether any strobes extend past the end of the
cycle and changes the values accordingly.  Then the entries in
   outmin[] and outmax[] are calculated; this part of the program is a
direct translation of the occam original.

   dstr0() is a function to draw the top half of the waveform for a
strobe signal.  This consists of just underline characters and spaces.
The function is called by waves() , which draws the strobe signals.

   dstr1() is a companion function to dstr0() .  It draws the bottom
half of the waveform for a strobe signal, using underline characters,
strokes in both directions and spaces.  Both dstr0() and dstr1() are
passed a strobe number and extract their information from the arrays
start[] and stop[] .

   waves() is responsible for rendering the waveforms on pages 4 and 5.
It takes an argument, p , which determines whether it draws the read
cycle timing or the write cycle timing.  First of all, the width
available to show each Tstate is calculated, as is the total number of
states that can be shown.  These are stored in the variables chst and
nst .  Then the states are labelled across the top of the page, and the
   ProcClock waveform drawn underneath.  dstr0() and dstr1() are used to
render the strobes S0-S4 and MemWait .  The activity on the
   MemAD lines is rather more difficult to represent, as the bus can be
tristated.  Special inline code is used to draw these signals.  Either
the read or the write strobe is then drawn using dstr0() and
   dstr1() , according to the value of p .  A mark is added to indicate
the time (at the end of T5) when data are latched into the transputer.


   race() simply prints a warning message if the flag waitrace is true.
It is called by page1() .

   scrolll() adjusts leftst so as to scroll the waveform display to the
left.  The move is by about 15 characters.

   scrollr() adjusts leftst so as to scroll the waveform display to the
right.  Again, the move is by about 15 characters.

   load() is the routine which extracts a configuration from a saved
file.  The user is prompted for a filename, and given the chance to
abandon the load operation.  The file is then searched for a line
containing `Page 1'.  Subsequent lines are read in, and rudimentary
checks are made for validity.  Values are written into the structure a
as they are found.  This means that if the file is found to have bad
format partway through a load operation, the data in a will only be
partially valid.  In this case, the configuration is reset to default
configuration 31, and a message to that effect printed.  The program is
thus sensitive to the saved files being edited, although certain
operations are safe.  For example, all the pages in the saved file can
be deleted as long as page 1 remains intact and retains its header.
Modifying the contents of page 1 is, however, dangerous.

All the remaining functions deal with generating PostScript output.

   dot() converts a text string into a PostScript compatible format.
This principally involves inseting ` ' characters before open and close
parentheses.  The text is then printed out right justified to a margin
134 points in from the left hand edge of the page.  This routine is used
in printing the names of signals on the timing diagram.

   txt() prints a string at chosen x and y coordinates and is used for
all the other text to appear on the diagram.

   hup() prints a small upwards sloping diagonal line suitable for the
rising edges of waveforms.

   hdown() prints a downwards sloping line for the falling edges of
waveforms.

   alongl() prints a horizontal line one Tstate in length.

   alongs() prints a slightly shorter horizontal line.

   along() prints a still shorter horizontal line.  The waveforms are
all drawn by these last five functions, called in various sequences.

   dwave() draws a strobe signal using the information in start[] and
   stop[] , calling the above routines in an appropriate order.

   dops() is responsible for the creation of the entire PostScript file.
It obtains a filename, and in the same way as save() , checks whether or
not the file already exists before overwriting it.  It calculates the
number of points horizontally that each Tstate can occupy, and stores it
in pst .  It then generates the prologue for the PostScript file.  The
creation date is not set as there is no standard C library call to
obtain the current date.  When compiled for a particular host, however,
it would be trivial to add the small piece of machine dependent code
necessary.  The fonts used are `Helvetica' and `Helvetica Bold', which
should be supported by most output devices.  The page is turned through
ninety degrees so that the printing is done in landscape mode.  First
the Tstates are labelled, and then the waveforms drawn one at a time.
Unlike the output from pages 4 and 5, the read and write cycle timings
are presented here in one diagram.  dwave() is called to draw the simple
strobes, and the more complicated signals like ProcClock and
   MemAD are drawn separately.  A mark is added to show where the read
data are latched into the transputer.  The (empty) trailer is finally
written to the file and the file closed.


 Compilation

Since the program uses only standard library functions and header files,
it can be compiled directly on most machines.  The program has been
tested on compilers with 32 bit int s and with 16 bit int s.

EPROM HEX PROGRAM NOTES
-----------------------


 Introduction

Since the EPROM hex program needs to read in files at various stages
during its execution, it is impossible to make it completely
machine-independent.  Those parts of the program that deal with files
are therefore isolated in a separate module.  There is one portability
issue that has not been addressed: the program will produce invalid
output files if compiled for a machine which does not use the ASCII code
for its printable characters.

It will be assumed that the reader of this chapter has a listing of the
program to hand.


 Defined constants

Constants are defined for the four files that the program has to deal
with and the three output data formats.  CRLF is a string containing an
ASCII carriage return and line feed sequence; escape codes such as n do
not always translate to the same characters across all machines.
MAXCONF is the maximum size in words of a ``configuration table''.
Configuration tables are discussed in the data sheets for the IMS T414
and IMS T800 transputers and in the documentation for the external
memory interface program.  packet and packet give the buffer size used
by the loader programs that distribute code across transputer networks.
The remaining definitions are offsets into the workspace used by the
initialisation code which is ultimately written into the EPROM.


 Variables

   (*outbyte)() is a pointer to a function which is called with each
byte of data that is to be written.  By changing the value of this
pointer, the data can be directed to the desired sink.

   ofp is the handle of the file to which output is being written.

   omode indicates the data format selected for output.  It takes on one
of the values IHEX , IEHEX , or PHEX .

   obuf is a buffer for 16 bytes of output data.  The first free byte in
the buffer is the one indexed by obptr .

   oadd is the address to be sent to the EPROM programmer of the next
byte to be processed.  It is incremented by each call to a routine
pointed to by outbyte() .

   sadd is the start address to be sent to the EPROM programmer of the
block that is being constructed in obuf .  Thus oadd is the sum of sadd
and obptr .

   startw is the start address of the block that is to be output to the
programmer.

   endw is one more than the last address in the block that is being
output to the programmer.

   blocks is a flag which is set to 1 when block mode is enabled.

   type is the processor type code, extracted from the main procedure
file given to the program.  The types which the program currently
supports are `2', for the T212 16-bit processor, `4' for the T414 32-bit
processor and `8', for the T800 32-bit floating-point processor.  The
value of type is used as an index into the following arrays, which
should be extended if additional processors are to be supported:

   bpw[] is the wordlength of the processor in bytes (``bytes per
word'').

   bsm[] is the byte select mask for the processor, i.e.  a mask which
extracts those bits in an address which select the byte within the word.

   valid[] is an array of flags which indicate when a given processor
number is valid.

   mint[] is the value of MostNeg INT for the processor, i.e.
 .

   confb[] is the length of a configuration table for the processor in
bytes.

   confw[] is the length of a configuration table for the processor in
words.

   max is the limit on the size of a loader program for the processor.

   memstart[] is the number of words reserved by the processor at the
bottom of memory.

   modes[] contains strings describing the available output formats.

   space holds the total computed RAM requirement of the code being
loaded into EPROM.

   workspace is the total workspace memory requirement of the code.

   vec is the amount of separate vector space required by the main
procedure.

   SC is the offset into the main procedure where it should be entered.

   end is the EPROM address where the PROGRAM data finish (and hence
where the main procedure starts).

   start is the EPROM offset of the start of the initialisation code.

   jmpdest is the destination of the jump instruction which is placed at
the top of the EPROM.  This will either be the same as start or will be
the address of a further jump instruction.  The latter case occurs when
a two-byte instruction is insufficient to reach
   start from the end of the EPROM.

   files[][] holds the names of the three files which the program may
need to open.

   cfa is a flag which is set to 1 if the user requests that code to
copy away the bottom 600 bytes of memory on initialisation be inserted.
This is necessary if it is intended to analyse the target processor with
a debugging tool.

   ramsize holds the amount of RAM attached to the target processor,
measured in bytes.

   tsize holds the size of the final EPROM.

   counter counts the bytes that are output.  It is incremented on each
call to a function pointed to by outbyte() .

   hicount holds the highest value that count reaches.  It is thus the
total number of bytes that are to be programmed into the EPROM.

   bytesel holds the selection of bytes that are to be output.  Bits in
its value are set according to whether the corresponding byte is to be
sent.


 Functions

   main() begins by setting omode to its default value of IHEX .  It
then parses its command line arguments by concatenating them into a
single string which is then stepped through one character at a time.
Filenames are copied into the relevant element of files[][] and omode ,
   cfa and blocks are set when their controlling switches are
encountered.  tsize and ramsize are also set.  If, when the entire
command line has been processed, no EPROM size has been set or no main
procedure filename has been found, an error is reported.  The other two
input files are optional.

If cfa is set, the program will need to know the total amount of RAM in
the target system --- this is so that it can compute the destination
address for the copy operation.  The value entered is tested to
determine whether it is a power of two; if it is not, the user is
warned.  The twin motivations behind this are that most systems have
just one or two banks of memory devices, so the total memory size is a
power of two and that the user may enter, for example, ``1000K'',
thinking that this is the same as one megabyte.  The memory size in
bytes is stored in ramsize and echoed to the screen for verification.

The function it() is then called to construct the EPROM contents and
produce the output files.

   prog() reads in a PROGRAM file, passing its contents to the function
pointed to by outbyte() .  The PROGRAM file has no header that must be
processed, and so this function simply checks that the file could be
opened and then passes on to rcode() .

   sc() reads a main procedure file, extracting from the header
information which it requires.  The format is that produced by the IBOOT
tool with the -R (omit bootstrap) option.  The format is as follows:

INT32     descriptor string length
[]BYTE    descriptor string
INT32     id string length
[]BYTE    id string
INT32     target processor
INT32     version number
INT32     scalar workspace requirement in words
INT32     vector workspace requirement in words (version 10 files only)
INT32     program entry point offset in bytes
INT32     program code size in bytes
[]BYTE    program code

The descriptor string length is read in; if the value is unreasonably
large, it is likely that the file is of the wrong type and so an error
message is printed.  If value is reasonable, the string itself is read.
The procedure is repeated for the id string.  The information in the
strings is not used.

The processor type is then read in and checked for validity using the
array valid[] .  Then the version number and workspace requirement are
read in.  If the version number is 10 then the separate vector space
requirement is read; otherwise, the version number must match the
processor type.  Finally the entry point and code length are read, and
   rcode() is called to load the code block, sending the data to the
function pointed to by outbyte() .

   readint32() is used by sc() to assemble four consecutive bytes from
the input file into a single long integer.

   conf() extracts the configuration table from a file saved by the
external memory interface program.  It reads in lines until it finds the
``Page 6'' identifier.  The three subsequent blank lines are skipped and
than the data are read into the array z[] bit by bit.  If an
inconsistency is detected at any point, the routine jumps to the label
   conf otherwise the configuration words are output via outword() .
Note that the use of the z[] array as a buffer is necessary as the data
are output in a different order from that in which they appear in the
input file.

   openf() calls the external function popen to open the requested file.
The opening is done in text mode for a configuration file and in binary
mode otherwise.

   blankconf() produces a null configuration.  This is called instead of
conf() if no configuration file was specified on the command line.

   outword() calls outbyte() a number of times appropriate to the word
length of the target processor.

   rcode() passes all the remaining bytes from the file whose handle it
is given as argument to the function pointed to by outbyte() , and
closes the file.

   instsize() computes the total number of bytes needed to code an
instruction whose operand is passed to the function.  The result is
obtained recursively: if the operand is in the range 0...15 inclusive
(the test op is false) then the result is 1; otherwise the length is one
more than the number to encode the operand, complemented if it is
negative, shifted right four places.

   codeop() works by a similar method; it generates the code sequence
required for an instruction by selecting a PFIX or NFIX instruction as
necessary and recursing.  The algorithm is described in ``The Transputer
Instruction Set --- A Compiler Writer's Guide''.

   bootcode() generates the transputer initialisation code that is to be
included in the EPROM.  It calls codeop() to assemble each instruction.
The instruction codes are defined in the header file ``m.h''.  If any
changes are contemplated to this routine great care should be taken as
an error in the initialisation code can have disastrous consequences for
the reliability of the target system.  The function instsize() is called
to find the offset required for the forwards jump instructions; the
backward jump offsets are computed by recording the value of counter at
the desired destination and subtracting the value of counter at the
beginning of the jump instruction.  The value is then modified in a
while loop to compensate for the length of the jump instruction itself.

At the end, the code is padded to a word boundary and the sizes of the
various data areas required are calculated.

   bounce() is used to insert an extra jump instruction between the
initialisation code and the configuration table.  This will be necessary
if the length of the jump instruction to reach from MostPos INT-1 to the
start of the initialisation code exceeds the two bytes available.  The
routine first checks whether the extra jump is needed; if it is the
correct length is calculated and the code inserted.  The code is padded
to the next word boundary.  The routine returns with jmpdest set to the
value of counter at the start of the initialisation code if no jump was
inserted, and to the inserted jump if one was.

   entryjmp() generates the jump from the reset location (MostPos INT-1)
prefixed by two zero bytes.  This ensures correct positioning with both
16- and 32-bit processors.

   roundup() pads the code to the next 4-byte boundary with zero bytes.

   pass() is the orchestrator of the EPROM code generation.  It calls in
order the functions prog() , sc() , bootcode() , bounce() , conf() and
entryjmp() , recording the correct values of end and start as it goes.

   null() is one of the functions to which outbyte() may point.  It has
no action but to increment counter and oadd .

   icsum() computes the ``Intel checksum'' of a sequence of bytes.  This
is the two's complement of the modulo 256 sum of the bytes.

   send() is the other function to which outbyte() can point.  It checks
whether oadd is between startw and endw (i.e.  whether it is in the
current block) and whether the byte selector of the current address is
one of those chosen in bytesel .  If these conditions are satisfied, a
test is made to see if the current address is in the same segment (64
kilobyte page) as the starting address for the record that is currently
being constructed.  If this is the case and Intel extended hex output
has been selected then the current record must be output by a call to
flush() and a type 02 ``change of segment'' record sent.  Otherwise the
byte to be output is appended to the output buffer obuf .  If the buffer
is now full, it is emptied by calling flush() .  oadd and counter are
both incremented.

   flush() writes the current record buffer out to the file specified in
ofp .  If the output mode is one of the Intel hex types, the checksum is
appended to the record and putihln called.  In the simple hex dump mode,
the address of the start of the block, sadd , is printed, followed by
the bytes of data.  The buffer pointer is reset to zero.

   endtx() sends an end-of-transmission record appropriate to the output
format in use.  This is null for the simple hex dump mode.

   putihln() outputs an Intel hex record.  It adds the opening delimitor
(a colon) and the trailing delimiter ( CRLF ).

   it() provides the user interface to the program.  It begins by
finding the total EPROM space required by calling pass() with outbyte()
set to null() .  hicount is set to the highest value that counter
reaches.  At this stage the various ROM and RAM requirements are known
and so are printed out.  If the RAM requirement for the main procedure
is greater than the value given in the
   max table entry for the target processor, a warning is given that the
value is too large for the procedure to be used as a loader.  The
selected output format is printed for verification.  The value of tsize
is checked to ensure that the generated code will fit in the final
EPROM; an error is generated if there is not enough space.

If block mode is enabled ( blocks equal to 1) the block number is
printed and the user asked for addresses specifying the area of EPROM to
be programmed and for the byte selection.  These are stored in starto ,
startw , endw and bytesel .  A warning is printed if the selection will
cause an overflow of the addresses available in the chosen output
format.  From these values the correct initial value of oadd is
determined.  A filename is obtained from the user, and ofp set to the
handle for the file.  outbyte() is set to send() so that output actually
occurs and pass() is called.  flush() is called to output the last
record and the output file is closed.  This entire procedure is repeated
until the user elects to stop.

If block mode is disabled, the variables startw and endw are set so that
all the bytes for the EPROM will be output.  Again a test for address
overflow is made and a file handle obtained.  pass() is called to output
the data and flush() is called to write the last record.  The file is
closed if necessary and the routine exits.


 Compilation

The program has been compiled on machines with both 16- and 32-bit INTs.
The header file ``m.h'' must be accessible by the compiler.  The
program must be linked with the function popen () whose source is in the
file ``popen.c''.